## Slide 1: Energy Management & Audit – An Overview
Notes: <number>

## Slide 2: WHAT IS ENERGY?
Mr.S. G. Bardiya, SITCOE, Yadrav
Definition: Energy is the capacity of a physical system to perform work. Energy exists in several forms such as heat, kinetic or mechanical energy, light, potential energy, electrical or other forms.
According to the law of conservation of energy, the total energy of a system remains constant, though energy may transform into another form.
For example, two billiard balls colliding, may come to rest, with the resulting energy converting to sound and perhaps a little bit of heat, at the point of collision.

## Slide 3: TYPES OF ENERGY
Mr.S. G. Bardiya, SITCOE, Yadrav
Mechanical energy Mechanical energy is energy that results from movement or the location of an object. Mechanical energy is the sum of Kinetic and Potential Energy.
Thermal energy Thermal energy or heat energy reflects the temperature difference between two systems.
Nuclear energy Nuclear energy is energy resulting from changes in the atomic nuclei or from nuclear
Chemical energy Chemical energy results from chemical reactions between atoms or molecules. There are different types of chemical energy, such as electrochemical energy etc.
Electromagnetic energy Electromagnetic energy is energy from light or electromagnetic waves.

## Slide 4: Definition of Energy Management
Mr.S. G. Bardiya, SITCOE, Yadrav
Energy Management is defined as “The strategy of adjusting and optimizing energy, using systems and procedures so as to reduce energy requirements per unit of output while holding constant or reducing total costs of producing the output from these systems”

## Slide 5
The Energy Management System
Mr.S. G. Bardiya, SITCOE, Yadrav

## Slide 6: The Objectives of Energy Management
Mr.S. G. Bardiya, SITCOE, Yadrav
To achieve and maintain optimum energy procurement and utilisation, throughout the organization
To minimise energy costs / waste without affecting production & quality
To minimise environmental effects.

## Slide 7: Energy Management Objectives Clarified
Mr.S. G. Bardiya, SITCOE, Yadrav
The basic objective of any Energy Management System is to answer five simple questions:
How much energy is consumed
How is the energy consumed
Where is the energy consumed
When is the energy consumed
What is the quality of the energy consumed
In order to address these queries Energy Audits are conducted. Lets understand audits -

## Slide 8: Definition of Energy Audit
Mr.S. G. Bardiya, SITCOE, Yadrav
As per Indian Energy Conservation Act 2001,
Energy Audit is defined as:
“the verification, monitoring and analysis of use of energy including submission of technical report containing recommendations for improving energy efficiency with cost benefit analysis and an action plan to reduce energy consumption “

## Slide 9: Why the Need for Energy Audit
Mr.S. G. Bardiya, SITCOE, Yadrav
The three top operating expenses are energy (both electrical and thermal), labour and materials.
Energy would emerge as a top ranker for cost reduction
primary objective of Energy Audit is to determine ways to reduce energy consumption per unit of product output or to lower operating costs
Energy Audit provides a “ bench-mark” (Reference point) for managing energy in the organization

## Slide 10: Types of Energy Audits
Mr.S. G. Bardiya, SITCOE, Yadrav
Preliminary Energy Audit
Targeted Energy Audit
Detailed Energy Audit
Notes: <number>
Type of Energy Audit
The type of Energy Audit to be performed depends on.
- the function and type of industry
- the depth to which final audit is needed, and
- the potential and magnitude of cost reduction desired
Thus Energy Audit can be classified into the following two types.
i) Preliminary Audit
ii) Detailed Audit

## Slide 11: Preliminary Energy Audit
Mr.S. G. Bardiya, SITCOE, Yadrav
Preliminary energy audit uses existing or easily obtained data
Establishes the energy consumption in the organization
Estimates the scope for saving
Identifies the most likely areas for attention
Identifies immediate(no cost or low cost) improvements
Sets a ‘reference point’
Identifies areas for more detailed study/measurement
Notes: <number>
2.  Collect the existing data e.g., a energy bills(volume/cost)
 Collect the Production output/records plant layouts using checklists
3. Analyse data:
 Find unit cost of energy (Rs./ kWh for all types)
 Find fixed and variable energy element
 Derive ‘energy Index’: energy cost/unit output ,energy cost/floor area
4. Formulate plan:
Formulate Immediate energy-saving actions: Where? How ? How much?
 Areas to investigate further
 Resources required for more detailed study
5. Actions and monitoring
Next steps (e.g. detailed audits), where needed

## Slide 12: Targeted Energy Audits
Mr.S. G. Bardiya, SITCOE, Yadrav
Targeted energy audits are mostly based upon the outcome of the preliminary audit results.
They provide data and detailed analysis on specified target projects.
As an example, an organization may target its lighting system or boiler system or compressed air system with a view to bring about energy savings.
Targeted audits therefore involve detailed surveys of the target subjects/areas with analysis of the energy flows and costs associated with those targets.

## Slide 13: Detailed Energy Audit
Mr.S. G. Bardiya, SITCOE, Yadrav
Detailed Energy Audit evaluates all systems and equipment which consume energy and the audit comprises a detailed study on energy savings and costs.
Detailed Energy Audit is carried out in 3 phases
  The Pre-audit Phase
  The Audit Phase
  The Post-Audit Phase

## Slide 14: The Ten Steps for Detailed Audit
Mr.S. G. Bardiya, SITCOE, Yadrav

## Slide 15
Mr.S. G. Bardiya, SITCOE, Yadrav

## Slide 16
Mr.S. G. Bardiya, SITCOE, Yadrav

## Slide 17
Mr.S. G. Bardiya, SITCOE, Yadrav

## Slide 18: Questions which an Energy Auditor should ask
Mr.S. G. Bardiya, SITCOE, Yadrav
What function does this system serve?
How does this system serve its function?
What is the energy consumption of this system?
What are the indications that this system is working properly ?
If this system is not working, how can it be restored to good working conditions/
How can the energy cost of this system be reduced?

## Slide 19
DETAILED ENERGY AUDIT
A TYPICAL INDUSTRIAL FORMAT
Energy Audit Team
Executive Summary –Scope & Purpose
Energy Audit Options & Recommendations
1.0 Introduction about the plant
  1.1 General Plant details and descriptions
  1.2 Component of production cost (Raw materials, energy, chemicals,
    manpower, overhead, others)
1.3 Major Energy use and Areas
2.0 Production Process Description
  2.1 Brief description of manufacturing process
  2.2 Process flow diagram and Major Unit operations
  2.3 Major Raw material Inputs, Quantity and Costs
3.0 Energy and Utility System Description
  3.1 List of Utilities
  3.2 Brief Description of each utility
      3.2.1 Electricity
      3.2.2 Steam
      3.2.3 Water
      3.2.4 Compressed air
      3.2.5 Chilled water
      3.2.6 Cooling water
Mr.S. G. Bardiya, SITCOE, Yadrav

## Slide 20
4.0 Detailed Process flow diagram and Energy& Material balance
    4.1 Flow chart showing flow rate, temperature, pressures of all input-
    Output streams
    Water balance for entire industry
5.0 Energy efficiency in utility and process systems
  5.1 Specific Energy consumption
  5.2 Boiler efficiency assessment
  5.3 Thermic Fluid Heater performance assessments
  5.4 Furnace efficiency Analysis
  5.5 Cooling water system performance assessment
  5.6 DG set performance assessment
  5.7 Refrigeration system performance
  5.8 Compressed air system performance
  5.9 Electric motor load analysis
  5.10 Lighting system
6.0 Energy Conservation Options & Recommendations
  6.1 List of options in terms of no cost, low cost, medium cost and high cost, annual energy savings and payback
  6.2 Implementation plan for energy saving measures/Projects
  ANNEXURE
  Al. List of instruments
  A2. List of Vendors and Other Technical details
Mr.S. G. Bardiya, SITCOE, Yadrav

## Slide 21
All Energy Audits require many measurements. Some common Instruments used are shown above
Mr.S. G. Bardiya, SITCOE, Yadrav

## Slide 22
Some more Energy Audit Instruments
Mr.S. G. Bardiya, SITCOE, Yadrav

## Slide 23: Identification of Energy Conservation Factors & Areas
Mr.S. G. Bardiya, SITCOE, Yadrav
Steps for conserving energy can be taken if we know the correct factors and areas to be studied and also details of fuels used.
These can be:
Energy generation
Energy distribution
Energy usage by processes
Fuel substitution

## Slide 24: Technical and Economic feasibility- Factors
Mr.S. G. Bardiya, SITCOE, Yadrav
Technology availability, space, skilled manpower, reliability, service,Impact of measure on safety, quality, production or process.Maintenance requirements and spares availability

## Slide 25: Energy Costs in Indian Scenario ?
Mr.S. G. Bardiya, SITCOE, Yadrav
Common Fuels
• Fuel oil,• Low Sulphur Heavy Stock (LSHS),• Light Diesel Oil (LDO),• Liquefied Petroleum Gas (LPG) • Coal,• Lignite,• Wood
Fuels Cost Inputs & Factors
Price at source, transport charge, type of transport,
Quality of fuel
Contaminations, Moisture, Energy content (GCV)
Power Costs
In India Electricity costs vary substantially not only from State to State, but also from city to city and also within consumer
to consumer – though power does the same work everywhere.
Reason:
Tariff Structure

## Slide 26: Understanding energy costs
Mr.S. G. Bardiya, SITCOE, Yadrav
An industrial energy bill summary
Conversion to common unit of energy

## Slide 27: Benchmarking
Mr.S. G. Bardiya, SITCOE, Yadrav
Benchmarking can be a useful tool for understanding energy consumption patterns in the industrial sector and also to take requisite measures for improving energy efficiency.
FACTORS INVOLVED:
  Scale of operation
  Vintage of technology
  Raw material specifications and quality
  Product specifications and quality

## Slide 28: Benchmarking for Energy Performance
Mr.S. G. Bardiya, SITCOE, Yadrav
Internal Benchmarking
  Historical and trend analysis
External Benchmarking
  Across similar industries
    Scale of operation, vintage of technology, raw material specification and quality and product specification and quality

## Slide 29: Bench Marking Energy Performance
Mr.S. G. Bardiya, SITCOE, Yadrav
Quantification of fixed and variable energy consumption trends vis-à-vis production levels
Comparison of the industry energy performance w.r.t. various production levels (capacity utilization)
Identification of best practices (based on the external benchmarking data)
Scope and margin available for energy consumption and cost reduction
Basis for monitoring and target setting exercises
Notes: <number>
Benchmarking energy performance permits
Quantification of fixed and variable energy consumption trends vis-à-vis production levels
Comparison of the industry energy performance w.r.t. various production levels (capacity utilization)
Identification of best practices (based on the external benchmarking data)
Scope and margin available for energy consumption and cost reduction
Basis for monitoring and target setting exercises.

## Slide 30: Benchmarking parameters Production or Equipment Related
Mr.S. G. Bardiya, SITCOE, Yadrav
Gross production related
e.g. kWh/MT clinker or cement produced (Cement plant)
e.g. kWh/MT, kCal/kg, paper produced (Paper plant)
Equipment / utility related
e.g. kWh/ton of refrigeration (on Air conditioning plant)
e.g. kWh /litre in a diesel power generation plant.

## Slide 31: Measuring Energy Performance
Mr.S. G. Bardiya, SITCOE, Yadrav
Production Factor = Current year’s production
Reference year’s production
Reference Year Equivalent Energy Use
The reference year’s equivalent energy use (or reference year equivalent) is the energy that would have been used to produce the current year’s production output.
The reference year equivalent is obtained by multiplying the reference year energy use by the production factor (obtained above)
Reference year equivalent = Reference year energy use x Production factor
Plant Energy Performance is the improvement or deterioration from the reference year. It is a measure of plant’s energy progress.
Plant energy performance = Reference year equivalent – Current year’s energy x 100
Reference year equivalent

## Slide 32: Maximizing System Efficiencies - Some Measures
Mr.S. G. Bardiya, SITCOE, Yadrav
Replace pumps, fans, air compressors, refrigeration compressors, boilers, furnaces, heaters and other energy conservation equipment, wherever significant energy efficiency margins exist
Eliminate steam leakages by trap improvements
Maximize condensate recovery
Adopt combustion controls for maximizing combustion efficiency

## Slide 33: Matching Energy Usage to Requirement
Mr.S. G. Bardiya, SITCOE, Yadrav
The mismatch between equipment capacity and user requirement often leads to inefficiencies due to part load operations, wastages etc. It is thus essential that proper energy matching studies are carried out & actions implemented.
Examples :
  Eliminate throttling
  Eliminate damper operations
  Fan resizing for better efficiency.
  Moderation of chilled water temperature for process chilling needs

## Slide 34: Optimising Energy Input Requirement
Mr.S. G. Bardiya, SITCOE, Yadrav
In order to ensure that the energy given to the system is being put to optimal use, site specific measures and checks should be carried out regularly.
EXAMPLES:
Shuffling of compressors to match needs.
Periodic review of insulation thickness
Identify potential for heat exchanger networking and process integration.

## Slide 35: Fuel and Energy Substitution – key steps towards conservation
Mr.S. G. Bardiya, SITCOE, Yadrav
Fuel substitution
Replacement of coal by coconut shells, rice husk etc
Replacement of LDO by LSHS
Energy substitution
Replacement of electric heaters by steam heaters
Replacement of steam based hot water by solar systems

## Slide 36
THANK YOU
Mr.S. G. Bardiya, SITCOE, Yadrav