## Slide 1: Chapter Outline
Shigley’s Mechanical Engineering Design

## Slide 2: Failure Examples
Failure of truck driveshaft spline due to corrosion fatigue
Shigley’s Mechanical Engineering Design
Fig. 5–1

## Slide 3: Failure Examples
Impact failure of a lawn-mower blade driver hub.
The blade impacted a surveying pipe marker.
Shigley’s Mechanical Engineering Design
Fig. 5–2

## Slide 4: Failure Examples
Failure of an overhead-pulley retaining bolt on a weightlifting machine.
A manufacturing error caused a gap that forced the bolt to take the entire moment load.
Shigley’s Mechanical Engineering Design
Fig. 5–3

## Slide 5: Failure Examples
Chain test fixture that failed in one cycle.
To alleviate complaints of excessive wear, the manufacturer decided to case-harden the material
(a) Two halves showing brittle fracture initiated by stress concentration
(b) Enlarged view showing cracks induced by stress concentration at the support-pin holes
Shigley’s Mechanical Engineering Design
Fig. 5–4

## Slide 6: Failure Examples
Valve-spring failure caused by spring surge in an oversped engine.
The fractures exhibit the classic 45 degree shear failure
Shigley’s Mechanical Engineering Design
Fig. 5–5

## Slide 7: Static Strength
Usually necessary to design using published strength values
Experimental test data is better, but generally only warranted for large quantities or when failure is very costly (in time, expense, or life)
Methods are needed to safely and efficiently use published strength values for a variety of situations
Shigley’s Mechanical Engineering Design

## Slide 8: Stress Concentration
Localized increase of stress near discontinuities
Kt is Theoretical (Geometric) Stress Concentration Factor
Shigley’s Mechanical Engineering Design

## Slide 9: Theoretical Stress Concentration Factor
Graphs available for standard configurations
See Appendix A–15 and A–16 for common examples
Many more in Peterson’s Stress-Concentration Factors
Note the trend for higher Kt at sharper discontinuity radius, and at greater disruption
Shigley’s Mechanical Engineering Design

## Slide 10: Stress Concentration for Static and Ductile Conditions
With static loads and ductile materials
  Highest stressed fibers yield (cold work)
  Load is shared with next fibers
  Cold working is localized
  Overall part does not see damage unless ultimate strength is exceeded
  Stress concentration effect is commonly ignored for static loads on ductile materials
Stress concentration must be included for dynamic loading (See Ch. 6)
Stress concentration must be included for brittle materials, since localized yielding may reach brittle failure rather than cold-working and sharing the load.
Shigley’s Mechanical Engineering Design

## Slide 11: Need for Static Failure Theories
Uniaxial stress element (e.g. tension test)
Multi-axial stress element
  One strength, multiple stresses
  How to compare stress state to single strength?
Shigley’s Mechanical Engineering Design

## Slide 12: Need for Static Failure Theories
Failure theories propose appropriate means of comparing multi-axial stress states to single strength
Usually based on some hypothesis of what aspect of the stress state is critical
Some failure theories have gained recognition of usefulness for various situations
Shigley’s Mechanical Engineering Design

## Slide 13: Maximum Normal (Principal) Stress Theory
Theory: Yielding begins when the maximum principal stress in a stress element exceeds the yield strength.
For any stress element, use Mohr’s circle to find the principal stresses.
Compare the largest principal stress to the yield strength.
Often the first theory to be proposed by engineering students.
Is it a good theory?
Shigley’s Mechanical Engineering Design

## Slide 14: Maximum Normal (Principal) Stress Theory
Experimental data shows the theory is unsafe in the 4th quadrant.
This theory is not safe to use for ductile materials.
Shigley’s Mechanical Engineering Design

## Slide 15: Maximum Shear Stress Theory (MSS)
Theory: Yielding begins when the maximum shear stress in a stress element exceeds the maximum shear stress in a tension test specimen of the same material when that specimen begins to yield.
For a tension test specimen, the maximum shear stress is 1 /2.
At yielding, when 1 = Sy, the maximum shear stress is Sy /2 .
Could restate the theory as follows:
  Theory: Yielding begins when the maximum shear stress in a stress element exceeds Sy/2.
Shigley’s Mechanical Engineering Design

## Slide 16: Maximum Shear Stress Theory (MSS)
For any stress element, use Mohr’s circle to find the maximum shear stress. Compare the maximum shear stress to Sy/2.
Ordering the principal stresses such that 1 ≥2 ≥3,
Incorporating a design factor n
Or solving for factor of safety
Shigley’s Mechanical Engineering Design

## Slide 17: Maximum Shear Stress Theory (MSS)
To compare to experimental data, express max in terms of principal stresses and plot.
To simplify, consider a plane stress state
Let A and B represent the two non-zero principal stresses, then order them with the zero principal stress such that 1 ≥2 ≥3
Assuming A ≥B there are three cases to consider
  Case 1: A ≥B ≥
  Case 2: A ≥ ≥B
  Case 3: 0 ≥A ≥ B
Shigley’s Mechanical Engineering Design

## Slide 18: Maximum Shear Stress Theory (MSS)
Case 1: A ≥B ≥
  For this case, 1 = A and 3 = 0
  Eq. (5–1) reduces to A ≥ Sy
Case 2: A ≥ ≥B
  For this case, 1 = A and 3 = B
  Eq. (5–1) reduces to A − B ≥ Sy
Case 3: 0 ≥A ≥ B
  For this case, 1 =  and 3 = B
  Eq. (5–1) reduces to B ≤ −Sy
Shigley’s Mechanical Engineering Design

## Slide 19: Maximum Shear Stress Theory (MSS)
Plot three cases on principal stress axes
Case 1: A ≥B ≥
  A ≥ Sy
Case 2: A ≥ ≥B
  A − B ≥ Sy
Case 3: 0 ≥A ≥ B
  B ≤ −Sy
Other lines are symmetric cases
Inside envelope is predicted safe zone
Shigley’s Mechanical Engineering Design
Fig. 5–7

## Slide 20: Maximum Shear Stress Theory (MSS)
Comparison to experimental data
Conservative in all quadrants
Commonly used for design situations
Shigley’s Mechanical Engineering Design

## Slide 21: Distortion Energy (DE) Failure Theory
Also known as:
  Octahedral Shear Stress
  Shear Energy
  Von Mises
  Von Mises – Hencky
Shigley’s Mechanical Engineering Design

## Slide 22: Distortion Energy (DE) Failure Theory
Originated from observation that ductile materials stressed hydrostatically (equal principal stresses) exhibited yield strengths greatly in excess of expected values.
Theorizes that if strain energy is divided into hydrostatic volume changing energy and angular distortion energy, the yielding is primarily affected by the distortion energy.
Shigley’s Mechanical Engineering Design
Fig. 5–8

## Slide 23: Distortion Energy (DE) Failure Theory
Theory: Yielding occurs when the distortion strain energy per unit volume reaches the distortion strain energy per unit volume for yield in simple tension or compression of the same material.
Shigley’s Mechanical Engineering Design
Fig. 5–8

## Slide 24: Deriving the Distortion Energy
Hydrostatic stress is average of principal stresses
Strain energy per unit volume,
Substituting Eq. (3–19) for principal strains into strain energy equation,
Shigley’s Mechanical Engineering Design

## Slide 25: Deriving the Distortion Energy
Strain energy for producing only volume change is obtained by substituting av for 1, 2, and 3
Substituting av from Eq. (a),
Obtain distortion energy by subtracting volume changing energy, Eq. (5–7), from total strain energy, Eq. (b)
Shigley’s Mechanical Engineering Design

## Slide 26: Deriving the Distortion Energy
Tension test specimen at yield has 1 = Sy and 2 = 3 =0
Applying to Eq. (5–8), distortion energy for tension test specimen is
DE theory predicts failure when distortion energy, Eq. (5–8), exceeds distortion energy of tension test specimen, Eq. (5–9)
Shigley’s Mechanical Engineering Design

## Slide 27: Von Mises Stress
Left hand side is defined as von Mises stress
For plane stress, simplifies to
In terms of xyz components, in three dimensions
In terms of xyz components, for plane stress
Shigley’s Mechanical Engineering Design

## Slide 28: Distortion Energy Theory With Von Mises Stress
Von Mises Stress can be thought of as a single, equivalent, or effective stress for the entire general state of stress in a stress element.
Distortion Energy failure theory simply compares von Mises stress to yield strength.
Introducing a design factor,
Expressing as factor of safety,
Shigley’s Mechanical Engineering Design

## Slide 29: Octahedral Stresses
Same results obtained by evaluating octahedral stresses.
Octahedral stresses are identical on 8 surfaces symmetric to the principal stress directions.
Octahedral stresses allow representation of any stress situation with a set of normal and shear stresses.
Shigley’s Mechanical Engineering Design
Principal stress element with single octahedral plane showing
All 8 octahedral planes showing

## Slide 30: Octahedral Shear Stress
Octahedral normal stresses are normal to the octahedral surfaces, and are equal to the average of the principal stresses.
Octahedral shear stresses lie on the octahedral surfaces.
Shigley’s Mechanical Engineering Design
Fig. 5–10

## Slide 31: Octahedral Shear Stress Failure Theory
Theory: Yielding begins when the octahedral shear stress in a stress element exceeds the octahedral shear stress in a tension test specimen at yielding.
The octahedral shear stress is
For a tension test specimen at yielding, 1 = Sy , 2 = 3 = 0. Substituting into Eq. (5–16),
The theory predicts failure when Eq. (5–16) exceeds Eq. (5–17). This condition reduces to
Shigley’s Mechanical Engineering Design

## Slide 32: Failure Theory in Terms of von Mises Stress
Equation is identical to Eq. (5–10) from Distortion Energy approach
Identical conclusion for:
  Distortion Energy
  Octahedral Shear Stress
  Shear Energy
  Von Mises
  Von Mises – Hencky
Shigley’s Mechanical Engineering Design

## Slide 33: DE Theory Compared to Experimental Data
Plot von Mises stress on principal stress axes to compare to experimental data (and to other failure theories)
DE curve is typical of data
Note that typical equates to a 50% reliability from a design perspective
Commonly used for analysis situations
MSS theory useful for design situations where higher reliability is desired
Shigley’s Mechanical Engineering Design
Fig. 5–15

## Slide 34: Shear Strength Predictions
Shigley’s Mechanical Engineering Design
For pure shear loading, Mohr’s circle shows that A = −B = 
Plotting this equation on principal stress axes gives load line for pure shear case
Intersection of pure shear load line with failure curve indicates shear strength has been reached
Each failure theory predicts shear strength to be some fraction of normal strength
Fig. 5–9

## Slide 35: Shear Strength Predictions
Shigley’s Mechanical Engineering Design
For MSS theory, intersecting pure shear load line with failure line [Eq. (5–5)] results in
Fig. 5–9

## Slide 36: Shear Strength Predictions
Shigley’s Mechanical Engineering Design
For DE theory, intersection pure shear load line with failure curve [Eq. (5–11)] gives
Therefore, DE theory predicts shear strength as
Fig. 5–9

## Slide 37: Example 5-1
Shigley’s Mechanical Engineering Design

## Slide 38: Example 5-1
Shigley’s Mechanical Engineering Design

## Slide 39: Example 5-1
Shigley’s Mechanical Engineering Design

## Slide 40: Example 5-1
Shigley’s Mechanical Engineering Design

## Slide 41: Example 5-1
Shigley’s Mechanical Engineering Design

## Slide 42: Example 5-1
Shigley’s Mechanical Engineering Design

## Slide 43: Example 5-1
Shigley’s Mechanical Engineering Design
Fig. 5−11

## Slide 44: Example 5-1
Shigley’s Mechanical Engineering Design
Fig. 5−11

## Slide 45: Failure Theories for Brittle Materials
Experimental data indicates some differences in failure for brittle materials.
Failure criteria is generally ultimate fracture rather than yielding
Compressive strengths are usually larger than tensile strengths
Shigley’s Mechanical Engineering Design
Fig. 5−19

## Slide 46: Maximum Normal Stress Theory
Theory: Failure occurs when the maximum principal stress in a stress element exceeds the strength.
Predicts failure when
For plane stress,
Incorporating design factor,
Shigley’s Mechanical Engineering Design

## Slide 47: Maximum Normal Stress Theory
Plot on principal stress axes
Unsafe in part of fourth quadrant
Not recommended for use
Included for historical comparison
Shigley’s Mechanical Engineering Design
Fig. 5−18

## Slide 48: Brittle Coulomb-Mohr
Same as previously derived, using ultimate strengths for failure
Failure equations dependent on quadrant
Shigley’s Mechanical Engineering Design
Quadrant condition
Failure criteria
Fig. 5−14

## Slide 49: Brittle Failure Experimental Data
Coulomb-Mohr is conservative in 4th quadrant
Modified Mohr criteria adjusts to better fit the data in the 4th quadrant
Shigley’s Mechanical Engineering Design
Fig. 5−19

## Slide 50: Modified-Mohr
Shigley’s Mechanical Engineering Design
Quadrant condition
Failure criteria

## Slide 51: Example 5-5
Shigley’s Mechanical Engineering Design
Fig. 5−16

## Slide 52: Example 5-5
Shigley’s Mechanical Engineering Design

## Slide 53: Example 5-5
Shigley’s Mechanical Engineering Design

## Slide 54: Selection of Failure Criteria
First determine ductile vs. brittle
For ductile
  MSS is conservative, often used for design where higher reliability is desired
  DE is typical, often used for analysis where agreement with experimental data is desired
  If tensile and compressive strengths differ, use Ductile Coulomb-Mohr
For brittle
  Mohr theory is best, but difficult to use
  Brittle Coulomb-Mohr is very conservative in 4th quadrant
  Modified Mohr is still slightly conservative in 4th quadrant, but closer to typical
Shigley’s Mechanical Engineering Design

## Slide 55: Selection of Failure Criteria in Flowchart Form
Shigley’s Mechanical Engineering Design
Fig. 5−21