## Slide 1: Eng. 6002 Ship Structures 1
Intro to the Finite Element Method

## Slide 2: Introduction
In this lecture we will outline the basic ideas and features of the finite element method.
We will also introduce the 2D finite element called the constant stress triangle

## Slide 3: The Method
The basic concept for the FE method is similar to that for matrix frame analysis
  The structure can be represented as an assemblage of individual structural elements interconnected at a discrete number of nodes
This subdivision is natural for beam elements connected at a number of joints, but for panels the subdivision is not as obvious
  We have to divide the panel into a number of artificial elements
  These are known as finite elements and generally take the shape of a triangle or rectangle

## Slide 4: The Method
The accuracy of the FE method increases with the number of elements used (but this also computationally expensive)
A graded mesh is used that is more dense in areas of higher stress concentration (eg cut-outs)
Experience with similar structures is often necessary, but there are also automatic refinement algorithms to optimise the number of mesh elements (and their locations).

## Slide 5: The Method
We will consider only two-dimensional stress elements. These are sufficient for hull module analysis and for the analysis of individual panels of plating
Three-dimensional elements are usually only required for very local and detailed stress analysis

## Slide 6: The Constant Stress Triangle (CST)
To illustrate the way that finite elements are formulated, we will look at an element called the constant stress triangle (cst).
This is a standard 2D element that is available in most finite element models.
Consider a 2D element which is only able to take in-plane stress. The three corners of the triangle can only move in the plane.

## Slide 7: The Constant Stress Triangle (CST)
This element is extremely versatile:
  Almost any 2D shape can be represented by an assemblage of triangles
  3D curved surfaces can also be modelled

## Slide 8: The Constant Stress Triangle (CST)
For this element the force balance is;
F = Ke δ
{6} =[6x 6]{6}

## Slide 9: The Method
We use steps similar to that for matrix analysis
Step 1. Select a suitable displacement function:
  We represent each displacement component by a linear polynomial in x and y.
    U = c1 + c2(x) + c3(y)
    V = c4 + c5(x) + c6(y)
  And the displacement function in matrix form is given by

## Slide 10: The Method
Step 2: Find the Constants in C
The total displacement can be written by combining the 3 nodes of the cst
Where A is the connectivity matrix

## Slide 11: The Method
The unknown polynomial coefficients, C, can now be determined by inverting the connectivity matrix.
  C = A-1 δ
So, we can now express the unknown coefficients, C, in terms of the nodal displacements

## Slide 12: The Method
Step 3: Find the Strain on the element
We need the strain to get the stress, and the stress to get the stiffness.
The strain at any point in the element has three parts:

## Slide 13: The Method
Step 3: Find the Strain on the element
We substitute the polynomials for u and v:

## Slide 14: The Method
Step 3: Find the Strain on the element
So:
And in matrix form:

## Slide 15: The Method
Step 3: Find the Strain on the element
This can also be written as:
ε = GC
Or ε = GA-1δ
Or ε = Bδ, where B is known as the strain coefficient matrix

## Slide 16: The Method
Step 4: Find expression for stress
For plane stress the relationship between stress and strain is:

## Slide 17: The Method
Step 4: Find expression for stress
In matrix notation:
Or σ(x,y) = Dε(x,y)
And σ(x,y) = DBδ, where D is the elasticity matrix

## Slide 18: The Method
Step 4: Find expression for stress
Finally, σ=Sδ, where S=DB

## Slide 19: The Method
Step 5: Obtain the element stiffness matrix
The element stiffness matrix is obtained by using the principle of virtual work

## Slide 20: Problem:
Find the stiffness matrix for the following cst element

## Slide 21: Problem:
Find the stiffness matrix for a cst element with nodes at (0.1,0.1), (0.5,0.2) and (0.1,0.3). The thickness is 0.01m and E = 200,000 MPa
Hint: use Matlab (or Maple) for the matrix operations