## Slide 1: Introduction to Finite Element Method
Mathematic Model
Finite Element Method
Historical Background
Analytical Process of FEM
Applications of FEM
Computer Programs for FEM

## Slide 2: 1. Mathematical Model
Physical Problems
Mathematical Model
Solution
Identify control variables
Assumptions (empirical law)
(1) Modeling
(2) Types of solution
 | Exact Eq. | Approx. Eq.
Exact Sol. | ◎ | ◎
Approx. Sol. | ◎ | ◎
Eq.
Sol.

## Slide 3
(3) Methods of Solution

## Slide 4
(3) Method of Solution
Classical methods
They offer a high degree of insight, but the problems are difficult or impossible to solve for anything but simple geometries and loadings.
B. Numerical methods
(I) Energy: Minimize an expression for the potential energy of the structure over the whole domain.
(II) Boundary element: Approximates functions satisfying the governing differential equations not the boundary conditions.
(III) Finite difference: Replaces governing differential equations and boundary conditions with algebraic finite difference equations.
(IV) Finite element: Approximates the behavior of an irregular, continuous structure under general loadings and constraints with an assembly of discrete elements.

## Slide 5
2. Finite Element Method
(1) Definition
FEM is a numerical method for solving a system of governing equations over the domain of a continuous physical system, which is discretized into simple geometric shapes called finite element.
Continuous system
Time-independent PDE
Time-dependent PDE
Discrete system
Linear algebraic eq.
ODE

## Slide 6
(2) Discretization
Modeling a body by dividing it into an equivalent
system of finite elements interconnected at a finite
number of points on each element called nodes.

## Slide 7
3. Historical Background

## Slide 8
Chronicle of Finite Element Method
Year
Scholar
Theory
1941
Hrennikoff
Presented a solution of elasticity problem using one-dimensional elements.
1943
McHenry
Same as above.
1943
Courant
Introduced shape functions over triangular subregions to model the whole region.
1947
Levy
Developed the force (flexibility) method for structure problem.
1953
Levy
Developed the displacement (stiffness) method for structure problem.
1954
Argyris & Kelsey
Developed matrix structural analysis methods using energy principles.
1956
Turner, Clough, Martin, Topp
Derived stiffness matrices for truss, beam and 2D plane stress elements. Direct stiffness method.
1960
Clough
Introduced the phrase finite element .
1960
Turner et. al
Large deflection and thermal analysis.
1961
Melosh
Developed plate bending element stiffness matrix.
1961
Martin
Developed the tetrahedral stiffness matrix for 3D problems.
1962
Gallagher et al
Material nonlinearity.

## Slide 9
Chronicle of Finite Element Method
Year
Scholar
Theory
1963
Grafton, Strome
Developed curved-shell bending element stiffness matrix.
1963
Melosh
Applied variational formulation to solve nonstructural problems.
1965
Clough et. al
3D elements of axisymmetric solids.
1967
Zienkiewicz et.
Published the first book on finite element.
1968
Zienkiewicz et.
Visco-elasticity problems.
1969
Szabo & Lee
Adapted weighted residual methods in structural analysis.
1972
Oden
Book on nonlinear continua.
1976
Belytschko
Large-displacement nonlinear dynamic behavior.
~1997
New element development, convergence studies, the developments of supercomputers, the availability of powerful microcomputers, the development of user-friendly general-purpose finite element software packages.

## Slide 10
4. Analytical Processes of Finite Element Method
(1) Structural stress analysis problem
Conditions that solution must satisfy
a. Equilibrium
b. Compatibility
c. Constitutive law
d. Boundary conditions
Above conditions are used to generate a system of equations
representing system behavior.
B. Approach
a. Force (flexibility) method: internal forces as unknowns.
b. Displacement (stiffness) method: nodal disp. As unknowns.
For computational purpose, the displacement method is more
desirable because its formulation is simple. A vast majority of
general purpose FE softwares have incorporated the displacement
method for solving structural problems.

## Slide 11
(2) Analysis procedures of linear static structural analysis
A. Build up geometric model
a. 1D problem
line
b. 2D problem
surface
c. 3D problem
solid

## Slide 12
B. Construct the finite element model
a. Discretize and select the element types
(a) element type
1D line element
2D element
3D brick element
(b) total number of element (mesh)
1D:
2D:
3D:

## Slide 13
b. Select a shape function
1D line element: u=ax+b
c. Define the compatibility and constitutive law
d. Form the element stiffness matrix and equations
(a) Direct equilibrium method
(b) Work or energy method
(c) Method of weight Residuals
e. Form the system equation
Assemble the element equations to obtain global system equation and introduce boundary conditions

## Slide 14
C. Solve the system equations
a. elimination method
Gauss’s method (Nastran)
b. iteration method
Gauss Seidel’s method
Displacement field
strain field
stress field
D. Interpret the results (postprocessing)
a. deformation plot
b. stress contour

## Slide 15
5. Applications of Finite Element Method
Structural Problem | Non-structural Problem
Stress Analysis - truss & frame analysis - stress concentrated problem Buckling problem Vibration Analysis Impact Problem | Heat Transfer Fluid Mechanics Electric or Magnetic Potential

## Slide 16
6. Computer Programs for Finite Element Method
 | 結構 | 非線性 | 最佳化 | 複合材料 | 碰撞分析 | 疲勞分析 | 機構分析 | 噪音分析 | 流力分析 | 模流分析 | 熱傳分析
ANSYS | ◎ |  | ◎ | ◎ |  |  |  | ◎ | ◎ |  | ◎
NASTRAN | ◎ |  | ◎ | ◎ |  |  |  | ◎ |  |  | ◎
ABAQUS | ◎ | ◎ |  |  | ◎ |  |  | ◎ |  |  | ◎
MARC | ◎ | ◎ |  |  | ◎ |  |  | ◎ |  |  | ◎
LS-DYNA3D |  |  |  |  | ◎ |  |  |  |  |  | 
MSC/DYNA |  |  |  |  | ◎ |  |  |  |  |  | 
ADAMS/ DADS |  |  |  |  |  |  | ◎ |  |  |  | 
COSMOS | ◎ |  | ◎ | ◎ |  |  |  |  | ◎ |  | ◎
MOLDFLOW |  |  |  |  |  |  |  |  |  | ◎ | 
C-FLOW |  |  |  |  |  |  |  |  |  | ◎ | 
PHOENICS |  |  |  |  |  |  |  |  | ◎ |  | ◎