## Slide 1: The Finite Element Method
General Overview

## Slide 2: General Overview
widespread use in many engineering applications
Applications of FEM in Engineering
Mechanical/Aerospace/Civil/Automobile Engineering
Structure analysis (static/dynamic,linear/nonlinear)
Thermal/fluid flows
Electromagnetics
Geomechanics
Biomechanics
...

## Slide 3: General Overview
examples
  conduction heat transfer, solve for the temperature distribution throughout the body with known boundary conditions and material properties
  fluid mechanics problems range from steady inviscid incompressible flow to complex viscous compressible flow,

## Slide 4: General Overview
  acoustics uses finite element and boundary element numerical methods
  electromagnetic solution for magnetic field strength provide insight to the design of electromagnetic devices
  capabilities extended to include fluid-structure interactions, convective heat transfer
  Bio-mechanics-bone structural analysis, blood flow in blood vessels

## Slide 5: General Overview
Finite element method is a numerical method of solving a system of governing equations over the domain of a continuous physical system
method applies the many fields of science and engineering
for engineering use, fields of continuum mechanics and the theory of elasticity provide the governing equations

## Slide 6
Why numerical method
Most engineering problem involve solution of
governing differential equations.

## Slide 7
For heat transfer, torsion of shafts, irrotational
flow, seepage through porous media

## Slide 8
Solution of differential equation is tedious and
some times impossible
Complex geometry, boundary conditions, loading conditions and material

## Slide 9: General Overview
Finite element method can be summarized in the following steps:
  small parts called elements subdivide the domain of the solid structure
  elements assemble through interconnections at a finite number of points (nodes) on each element
  assembly provides a model of the structure

## Slide 10: General Overview
  within each small domain, we assume a simple general solution to the governing equations
  solution for each element is a function of the unknown solutions at the nodes

## Slide 11
Fundamental concept of FEM
The fundamental concept of FEM is that continuous function of a continuum (given domain ) having infinite degrees of freedom is replaced by a discrete model, approximated by a set of piecewise continuous function having a finite degree of freedom.

## Slide 12
Since the discrete model has finite degrees of freedom, hence the method got the name ‘FINITE ELEMENTS’
Coined by Clough (1960).
Application of the general solution to all the elements results in a finite set of algebraic equations which are solved for the unknown nodal values
Applying boundary conditions solution for
is obtained.

## Slide 13: General Overview
sources of error
  assumed solution within the element is rarely the exact solution
    error between exact and assumed solution
    magnitude depends on the size of the elements relative to the solution variation
    in most cases, assumed solution converges to the correct as element size decreases

## Slide 14: General Overview
all solid structures could be modeled with three-dimensional solid elements, but for many cases this is overkill
many structures can be simplified by making some assumptions e.g. plane stress and plane strain assumptions, simple beam theory

## Slide 15: General Overview
elements are categorized as either structural or continuum
  structural elements include trusses, beams, plates and shells
    formulations are based on same assumptions as in their structural theories
    finite element solution is no more accurate than a solution using conventional beam or plate theory

## Slide 16: General Overview
  continuum elements are two- and three dimensional solid elements
    formulation based on the theory of elasticity (provides the governing equations for deformation and stress)
    Few closed form or numerical solutions exist for these problems

## Slide 17: Using a Computer Program
3 stages
  preprocessing
  processor
  postprocessing

## Slide 18: Using a Computer Program

## Slide 19: Using a Computer Program
preprocessing
  create model
    nodal point locations
    element selection
    nodal connectivities
    material properties
    displacement boundary conditions
    loads and load cases
  preprocessor assembles data into a format for execution

## Slide 20: Using a Computer Program
processor
  code that solves the system equations
    generates element stiffness matrices
    stores data in files
    assembles the structure stiffness matrix
    must provide enough displacement boundary conditions to prevent rigid body motion
  solution gives nodal displacements
  with element information, get strain and stress

## Slide 21: Using a Computer Program
postprocessing
  numeric output data difficult to use
  reduces data to graphic displays (contour plots, graphs)
  magnifies nodal displacements
  nodal displacements are single valued
  stress at a node can be multivalued if multiple elements are attached to the node
  (stress is found from within each element)

## Slide 22: Re-analysis/redsign
Postprocessing
  look at deformed displacements and check for consistency with expected results
  look at stresses and compare to approximate solution

## Slide 23: Re-analysis/redsign
Refine model by considering the results of the first analysis
  high stress and rapid variations reduce element size
  low stress  increase element size
  Redo analysis and check if results are converging

## Slide 26: Re-analysis/redsign
Figure 1-7 is a refined model of 1-6
  note how the maximum stress has increased
  convergence has not yet been achieved
Serious mistake if only one model is analyzed
  Figure 1-6 is in error by 23%, while Figure 1-7 is in error by 19%
There is no guarantee that results will be accurate