## Slide 1: Section 3: Implementation of Finite Element Analysis – the Constant Strain Triangle
Fundamental Concepts
Element Formulation
Assembly
Convergence and Other Issues
Examples
Will illustrate the details of these ideas in the context of a specific “simple” finite element called the Constant Strain Triangle (CST).

## Slide 2: Section 3: Implementation of FEA – the CST
Overview: What is Finite Element Analysis?
Assume a given problem is to be solved globally over some object. FEA proceeds as follows:
  Discretize the problem into a finite number of “local” approximate problems on regions called elements.
  Set up and solve each of the local approximate problems.
  Assemble the local solutions into a global solution.
  Check convergence. (If not converged, repeat steps #2 and #3.)
  Once converged, evaluate the solution.
Your responsibility! (Program does the rest.)

## Slide 3: Section 3.1: Fundamental Concepts
  An element is a small piece of an overall object characterized by:
    Its type (truss, beam, plate, solid, …)
    Its geometry (1D, 2D, or 3D; line, triangle, rectangle, tetrahedron, “brick”, …)
    Its nodes (corner, interior, …) and degrees of freedom (displacement, rotation, …)
    Its shape functions
What is an element?

## Slide 4: 3.1: Fundamental Concepts (cont.)
Nodes and Degrees of Freedom –
Elements are restricted in how they can behave.
  E.g., beam element from HW #1:
  No left/right motion allowed; only certain types of bending possible.
It is required that the complete range of possible behaviors be determined by the locations of the nodes, the basic behaviors allowed at each node (degrees of freedom), and the shape functions used.

## Slide 5: 3.1: Fundamental Concepts (cont.)
Required Properties of the Approximate Solution:
Well-posedness: the number of shape functions used in the approximate solution must equal the number of degrees of freedom.
  Degrees of freedom are the unknowns in the local problem; need one equation per unknown to get unique solution.
  E.g., Galerkin’s method:

## Slide 6: 3.1: Fundamental Concepts (cont.)
Required Properties of the Approximate Solution:
Differentiability: The shape functions must be continuous and have continuous derivatives up to an order consistent with the variational principle used.
  Defines behavior within element.
  In general, if nth order derivative is in variational principle, then shape functions must have continuous derivatives of order n-1.
  Prevents integrals from “blowing up” or becoming undefined.

## Slide 7: 3.1: Fundamental Concepts (cont.)

## Slide 8: 3.1: Fundamental Concepts (cont.)
  Example: 1D Axial Rod “dynamics”
  Variational principle before integrating by parts was
  Requires continuous 1st derivatives for u(x).
  Variational principle after integrating by parts was
  Requires continuous u(x).

## Slide 9: 3.1: Fundamental Concepts (cont.)
Required Properties of the Approximate Solution:
Completeness: approximate solution must be able to represent two special displacement states exactly –
  Rigid body motion: all points in element have same values of displacement.
  Constant strain state: all normal strains and shearing strains have a fixed value everywhere in the element.

## Slide 10: 3.1: Fundamental Concepts (cont.)
Required Properties of the Approximate Solution:
  Rigid body motions cannot create strain energy, so no strains present anywhere  constant displacement.

## Slide 11: 3.1: Fundamental Concepts (cont.)
Required Properties of the Approximate Solution:
  As element size becomes very small, expect internal strains to change very little at different points in element. If approximate solution cannot support this, expect problems in convergence.

## Slide 12: 3.1: Fundamental Concepts (cont.)
Required Properties of the Approximate Solution:
Compatibility: If two elements share a boundary, the shape functions must permit an appropriate level of continuity across the boundary.
  Prevents “gaps” or “kinks” from developing in global solution.
  Elements with this property are called conforming.
  For more complicated elements, compatibility may be required only at selected points on the boundary. (Such elements are called non-conforming.)

## Slide 13: 3.1: Fundamental Concepts (cont.)
  Example: Two constant strain triangles
  For element #1, displacements at P depend on coordinates of point and the values (u1, v1, u2, v2, u3, v3).
  For element #2, displacements at P depend on coordinates of point and the values (u1, v1, u2, v2, u4, v4).

## Slide 14: 3.1: Fundamental Concepts (cont.)
  Displacement continuity then requires
  at all points P and for all values of (u1, v1, u2, v2, u3, v3, u4, v4).
  Can show that this requirement will be satisfied if
  (Displacements on a boundary depend only upon the nodes on that boundary!)

## Slide 15: Section 3.2: Element Formulation
The Constant Strain Triangle element:
2D element used in plane stress and plane strain problems
Nominal thickness = h (small; can be variable)
Three corner nodes with coordinates (xi, yi)
Two degrees of freedom per node: (ui, vi)

## Slide 16: 3.2: Element Formulation (cont.)
Two approaches for generating shape functions:
“Interpolation approach”:
  Matrix-based method
  Works best for small numbers of d.o.f.
“Direct approach”:
  More geometric method
  Works best for higher-order elements
(Other methods also exist; will not discuss these much.)

## Slide 17: 3.2: Element Formulation (cont.)
Some basic ideas (for both approaches):
6 d.o.f. total  6 shape functions.
Fundamental unknowns are horizontal displacement u(x,y) and vertical displacement v(x,y).
 Each displacement expected to use 3 shape functions.
Rule of thumb: simple shape functions = better shape functions. (easier to integrate, more widely applicable, …)
For 2D elements, polynomials in x and y are most common choice for shape functions.
If you have derivatives of order n in your variational principle, it is best to choose your shape functions so that they can form a complete polynomial of order n. (Gives control over errors, faster convergence, …)

## Slide 18: 3.2: Element Formulation (cont.)
Pascal’s triangle
(Row n+1 based upon expansion of (x+y)n. )

## Slide 19: 3.2: Element Formulation (cont.)
“Interpolation approach”:
  Approximate u(x,y) and v(x,y) by complete 1st order polynomials:
  At each node, require u(xi,yi) = ui and v(xi,yi) = vi :
6 equations for the 6 unknowns!

## Slide 20: 3.2: Element Formulation (cont.)
“Interpolation approach”:
  Write this in matrix form:
  Solution (in symbolic form) is

## Slide 21: 3.2: Element Formulation (cont.)
“Interpolation approach”:
  Now, rewrite interpolation functions in matrix/vector form:
  Substitute previous result:
Matrix of shape functions!

## Slide 22: 3.2: Element Formulation (cont.)
“Interpolation approach”:
  For CST, can show that

## Slide 23: 3.2: Element Formulation (cont.)
Notes on “Interpolation approach”:
  This approach generalizes to different shapes, different node locations, and different numbers of d.o.f. (See Prob. 3.1 and 3.2 in Schaum’s Outline.)
  However, the matrix [C] is not always invertible for general choices of nodal locations.
  As number of d.o.f. increases, matrix inversion becomes more difficult, and thus exact functions become harder to determine.

## Slide 24: 3.2: Element Formulation (cont.)
“Direct approach”: Need two “facts” about shape functions –
  u(x,y) and v(x,y) are complete 1st order polynomials:
  Suppose I know the shape functions already:
Shape functions must be linear in both x and y.
Kronecker delta property

## Slide 25: 3.2: Element Formulation (cont.)
Visually, this looks like:

## Slide 26: 3.2: Element Formulation (cont.)
Consider the shape function corresponding to u1 :
Therefore, get a set of equations to solve:
Similar procedure to construct other shape functions.

## Slide 27: 3.2: Element Formulation (cont.)
Notes on “Direct approach”:
  This approach is more commonly used as number of d.o.f. and/or order of polynomials used increases.
  Works best if shape functions are computed on “standard” geometries – leads to so-called “isoparametric formulation”.

## Slide 28: 3.2: Element Formulation (cont.)
Check the required properties:
  Well-posedness: 6 d.o.f and 6 shape functions.
  Differentiability: Will show that only 1st derivatives show up in variational principle, so need continuous shape functions. 
  Completeness –
    Rigid body motion: Suppose


## Slide 29: 3.2: Element Formulation (cont.)
Check the required properties:
  Completeness –
    Constant strain: Can
  Continuity:

In fact, strain must be a constant !
Neither N3(x,y) nor N4(x,y) can influence what happens on the line between pt. 1 and pt. 2.
Only d.o.f. at pt. 1 and pt. 2 matter!


## Slide 30: 3.2: Element Formulation (cont.)
Next issue: deriving the approximate equations
Determine element (local) stiffness matrix
  Relates forces (stresses) to displacements (strains)
  Term is used for all elements, not just elastic ones
Determine element (local) force vector
  Includes both body forces and surface tractions
  Will change during the course of solving a problem

## Slide 31: 3.2: Element Formulation (cont.)
Goal: obtain approximate solution to 2D elasticity equations –
Galerkin, Calculus of Variations, Rayleigh-Ritz, …

## Slide 32: 3.2: Element Formulation (cont.)
Using Calculus of Variations (aka Principle of Virtual Displacements):
Key Idea: solve same problem locally –

## Slide 33: 3.2: Element Formulation (cont.)
New Goal: obtain approximate solution to 2D elasticity equations on each element –

## Slide 34: 3.2: Element Formulation (cont.)
Strain-Displacement Relations –
Relate u to ε as follows:
Using shape functions:
Derivative operator matrix,

## Slide 35: 3.2: Element Formulation (cont.)
Stress-Strain Relations –
Relate σ to ε as follows:
Using previous results:
Not the same as used in interpolation approach!

## Slide 36: 3.2: Element Formulation (cont.)
Element (Local) Stiffness Matrix –
Put these results into 1st term of PVD:
Element stiffness matrix, [k].

## Slide 37: 3.2: Element Formulation (cont.)
Notes on Element (Local) Stiffness Matrix –
The element stiffness matrix for any elastic element will follow the exact same process. (Details will change.)
Element stiffness matrix is symmetric.

## Slide 38: 3.2: Element Formulation (cont.)
Notes on Element (Local) Stiffness Matrix –
[k] for the CST element is:
(See Probs. 3.14, 3.19, and 3.40 in Schaum’s.)

## Slide 39: 3.2: Element Formulation (cont.)
Element (Local) Force Vector –
Evaluate 2nd and 3rd terms of PVD:
Element force vector (f)

## Slide 40: 3.2: Element Formulation (cont.)
Notes on Element (Local) Force Vector –
In general, b and t can depend upon position, so they are left inside of the integrals.
A “physical” interpretation of f:
Called equivalent nodal force

## Slide 41: 3.2: Element Formulation (cont.)
A “truss analogy” for elements –

## Slide 42: 3.2: Element Formulation (cont.)
Example –
Given: CST element shown has no body force and a surface traction applied to edge 23 expressed as
Required: Find (f).

## Slide 43: 3.2: Element Formulation (cont.)
Example –
Solution:

## Slide 44: 3.2: Element Formulation (cont.)
Example –
Solution:

## Slide 45: 3.2: Element Formulation (cont.)
Example –
Solution:

## Slide 46: Section 3: Implementation of FEA – the CST
Overview: What is Finite Element Analysis?
Assume a given problem is to be solved globally over some object. FEA proceeds as follows:
  Discretize the problem into a finite number of “local” approximate problems on regions called elements.
  Set up each of the local approximate problems.
  Assemble the local problems into a global problem.
  Solve the global problem and check convergence. (If not converged, repeat steps #2 and #3.)
  Once converged, evaluate the solution.

## Slide 47: Section 3.3: Assembly
  Each degree of freedom di in a given element corresponds to a unique degree of freedom Dk in the overall object.
   Each local stiffness matrix [k]e contributes to part of the global stiffness matrix of the object, [K].
  Also, each local force vector (f)e contributes to part of the global force vector of the object, (F).
Concept of assembly:
Global
Local

## Slide 48: 3.3: Assembly (cont.)
Concept of Assembly:
Assembly is not straight addition –

## Slide 49: 3.3: Assembly (cont.)
How is assembly done in FEA programs?
  Each element has an associated “map” that contains connectivity information; i.e., it links each local d.o.f. to corresponding global d.o.f. for the given element).
  Various names: “Connectivity vector”, “destination array”, “element-node array”, …
  For picture on Slide 2:

## Slide 50: 3.3: Assembly (cont.)
Pseudocode for Assembly:
For e = 1, numel ← sum over all elements
For i = 1, numdof(e) ← sum over all local d.o.f.
For j = i, numdof(e) ← local d.o.f.
ii = map(e,i); jj = map(e,j); ← get global d.o.f.
K(ii,jj) = K(ii,jj) + k(e,i,j); ← assemble [K]
Continue
F(ii) = F(ii) + f(e,i); ← assemble (F)
Continue
Continue

## Slide 51: 3.3: Assembly (cont.)
Assembly by hand:

## Slide 52: 3.3: Assembly (cont.)
Complication: what if local and global degrees of freedom are not parallel?
  Example: Roller support in global problem.
Easier to express boundary condition this way!

## Slide 53: 3.3: Assembly (cont.)
Create a set of “new” local coordinates that are parallel –
Can show that
Will also need to transform element force vector:

## Slide 54: 3.3: Assembly (cont.)
Stiffness matrix then transforms –
Can show that same approach works for other types of “transformations” (e.g., renumbering d.o.f., linking d.o.f, …)
These can now be assembled!

## Slide 55: Section 3.4: Boundary Conditions
  Traction boundary conditions used in PVD, but displacement boundary conditions aren’t.
  Shape functions must have Kronecker delta property Cannot “choose” them to satisfy
  Must enforce displacement boundary conditions on global problem!

## Slide 56: 3.4: Boundary Conditions (cont.)
  Three general techniques for enforcing displacement boundary conditions:
    Condensation
    Penalty Method
    Lagrange Multipliers
  In all methods, must discretize the boundary conditions to apply only at the nodes.

## Slide 57: 3.4: Boundary Conditions (cont.)
  Condensation –
  Idea: formally remove constrained d.o.f. from the calculation, but keep their effects on other d.o.f.

## Slide 58: 3.4: Boundary Conditions (cont.)
  Condensation –
  For each constrained d.o.f., remove (“condense out”) corresponding row and column from global equation.
New [K] matrix
New (F) vector
What if Di ≠ 0?

## Slide 59: 3.4: Boundary Conditions (cont.)
  Two possible situations where Di ≠ 0:
    Single-point boundary conditions: b.c. involves only one d.o.f.; at least one must be nonzero.

## Slide 60: 3.4: Boundary Conditions (cont.)
    Multi-point boundary conditions: b.c. involves more than one d.o.f.; may be zero or nonzero.

## Slide 61: 3.4: Boundary Conditions (cont.)
  Procedure:
  Re-number the d.o.f. to put constrained d.o.f. together.
  Write the constraints in matrix/vector form (see Slide 14).
  Solve for constrained d.of. in terms of regular d.o.f.:

## Slide 62: 3.4: Boundary Conditions (cont.)
  This defines a transformation into “new” coordinates:
  Substitute “new” coordinates into global problem :
  Multiply by [T] and rearrange:
New global stiffness matrix
New global force vector
“old” coordinates
“new” coordinates

## Slide 63: 3.4: Boundary Conditions (cont.)
  Notes on condensation –
  Very powerful method; can handle a variety of displacement boundary conditions exactly.
  Reduces bandwidth by eliminating d.o.f.
  If all boundary conditions are single-point, this method is equivalent to simply “condensing out” the constrained d.o.f. and adding in “extra” forces due to the imposed displacements.
  If there are many multi-point constraints, the process of re-numbering, transforming, and condensing can be very time-consuming.
  Condensation can sometimes be done at element level.

## Slide 64: 3.4: Boundary Conditions (cont.)
  Penalty Method –
  Idea: enforce a displacement boundary condition approximately by changing [K] and (F).

## Slide 65: 3.4: Boundary Conditions (cont.)
  Penalty Method –
  κ = stiffness of new spring; want
  Add new force to existing nodal force .
  Add to existing stiffness .
  Look at equation corresponding to d.o.f. D6 :
  Note: as κ gets bigger, approximation becomes better.

## Slide 66: 3.4: Boundary Conditions (cont.)
  General Theory of the Penalty Method –
  Assume boundary conditions in “standard form”
  Define an m by m “penalty matrix”
  Modify the global problem as follows:
m equations
Added stiffness
Added force

## Slide 67: 3.4: Boundary Conditions (cont.)
  Notes on the Penalty Method –
  Very easy to implement: no re-numbering, no transformations to apply, …
  Does not eliminate d.o.f., so no reduction in bandwidth.
  Assigning the penalty numbers κi can be tricky:
    Too low  poor approximation to boundary condition
    Too high  can create numerical problems (e.g., locking, ill-conditioning, …)

## Slide 68: 3.4: Boundary Conditions (cont.)
  Why “Penalty Method”? Look at variational principle:
  Set first variation to zero:
  Now, add in “penalty function”:
global approximate solution = “union” of all element solutions
penalizes errors in satisfying b.c.’s

## Slide 69: 3.4: Boundary Conditions (cont.)
  Lagrange Multipliers –
  Idea: add extra d.o.f. into the problem, and use these d.o.f. to enforce the boundary conditions.
  Note: Lagrange multipliers can be interpreted physically as constraint forces.
  Take first variation:
Lagrange multipliers
must equal zero
must equal zero

## Slide 70: 3.4: Boundary Conditions (cont.)
  Lagrange Multipliers –
  Get an augmented global problem:
  Advantage: very effective at handling multi-point constraints.
  Disadvantage: more d.o.f.  longer solution time.

## Slide 71: Section 3.5: Example Problem
  Given: Cantilevered beam with dimensions shown; rigidly fixed at x = 0; applied traction at x = 18. E = 27,000 ksi;  = 0.25 .
  Required: Using CST plane stress elements, find the approximate deflection of the free end at y = 0.

## Slide 72: 3.5: Example (cont.)
  Some preliminaries –
  Mesh the beam as shown:
  Exact solution is known:
  6 elements; 16 total d.o.f.; 4 constraints.

## Slide 73: 3.5: Example (cont.)
  Formulate the elements –
  Shape functions:
Element #1:
Element #2:

## Slide 74: 3.5: Example (cont.)
  Formulate the elements –
  Shape functions for other elements:
  Element #3 is simply Element #1 shifted from x = 0 to x = 6; thus, can “shift” each shape function:

## Slide 75: 3.5: Example (cont.)
  Element #4 = Element #2 shifted from x = 6 to x = 12:
  Element #5 = Element #1 shifted from x = 0 to x = 12:
  Element #6 = Element #2 shifted from x = 6 to x = 18:

## Slide 76: 3.5: Example (cont.)
  Formulate the elements –
  [B] matrix for Element #1:

## Slide 77: 3.5: Example (cont.)
  Formulate the elements –
  [B] matrix for Element #2:

## Slide 78: 3.5: Example (cont.)
  Other [B] matrices:
  Since Elements #3 and #5 are both simply shifts of Element #1, coefficients of x and y do not change.
  Likewise, Elements #4 and #6 are shifts of Element #2, so have same [B] matrices.

## Slide 79: 3.5: Example (cont.)
  Element stiffness matrices –
  Elastic matrix is:
  Since [B] and [C] are constant matrices, the volume integral for [k] reduces to

## Slide 80: 3.5: Example (cont.)
  For Element #1:

## Slide 81: 3.5: Example (cont.)
  For the other elements, we notice the following:
All elements have the same stiffness matrix!

## Slide 82: 3.5: Example (cont.)
  Only element force vector for Element #6:

## Slide 83: 3.5: Example (cont.)
  Assembly –
  Element #1:
  Element #2:

## Slide 84: 3.5: Example (cont.)
  Assembly –
  Stiffness matrix for #1 + #2 only:
  What about stiffness matrix for Element #3 + #4?
    Only real difference between #3+#4 and #1+#2 is the numbering of the d.o.f. – all shifted by 4
    Have same matrix for different d.o.f.

## Slide 85: 3.5: Example (cont.)
  Stiffness matrix for #3 + #4 only:
  Stiffness matrix for #5 + #6 only:

## Slide 86: 3.5: Example (cont.)
  Stiffness matrix for entire structure:

## Slide 87: 3.5: Example (cont.)
  Force vector for entire structure:

## Slide 88: 3.5: Example (cont.)
  Enforce constraints –
  Using condensation, you must simply eliminate the first 4 rows and columns of [K] and first 4 rows of (F):

## Slide 89: 3.5: Example (cont.)
  This can now be solved for the remaining d.o.f:
  Use this to interpolate the requested displacement:
Very poor approximation!

## Slide 90: 3.5: Example (cont.)
  What went wrong?
  Vertical d.o.f. are extremely stiff in this problem:
  (Changing aspect ratio will help.)
  CST is not a good element to model bending!
Dominant terms in equation. D14≈ D16= small number.