## Slide 1
Contents
Introduction
Types and configurations
Parts delivery at workstations
Various vibratory and non-vibratory devices for feeding and orientation
Product design for automated assembly

## Slide 2
Automated assembly refers to the use of mechanized and automated devices to perform the various assembly tasks in an assembly line or cell.
The vast majority of automated assembly systems are designed to perform a fixed sequence of assembly steps on a specific product.
Automated assembly is considered appropriate if it meets the following conditions:

## Slide 3
Automated Assembly – Application Characteristics
High product demand
Stable product design
The assembly consists of no more than a limited
number of components
4. The product is designed for automated assembly
Where is automated assembly appropriate

## Slide 4
Inline configuration

## Slide 5
Dial type configuration

## Slide 6
Carousel configuration

## Slide 7
Single-station configuration

## Slide 8
Parts delivery to workstations depends upon specific pieces of delivery equipment, particularly associated with automatic assembly.
These pieces of equipment are connected together to create the parts delivery system.
The following hardware for parts delivery consists of:

## Slide 9
Hopper—a container into which components are loaded at the workstation, and which passes components to the parts feeder.
Parts feeder—a mechanism used for removing components from the hopper, and passing them to the feed track; the parts feeder is often connected to the hopper to form one unit.
Selector and/or orientor—devices found on the feedtrack that establish the proper orientation of the components for the assembly workhead: a selector is a filter device that only-correctly oriented parts to pass; while an orientor re-orients parts that are not properly oriented initially on the feed track.

## Slide 10
Feed track—the pathway along which the components pass from the hopper and parts feeder to the assembly workhead, whilst maintaining proper orientation of the parts via selectors/orientors along the way; it generally operates by gravity, though powered feed tracks (operated by vibratory action or air pressure) may also be encountered.
Escapement and placement devices—devices used to remove components from the feedtrack (escapement), and to place them at the workstation for the assembly operation (placement); there are a number of different device designs to accomplish this.

## Slide 11
Hardware elements used to delivery parts to workstations

## Slide 12
Hopper and parts feeder

## Slide 13
Hopper and parts feeder

## Slide 14
Selector
Orientor devices used upon the feedtrack

## Slide 15
Horizontal placement device

## Slide 16
Vertical placement device

## Slide 17
Escapement device

## Slide 18
Pick-and-place mechanism (1)

## Slide 19
Pick-and-place mechanism (2)

## Slide 20
Design for Assembly
Includes part features such as chamfers and tapers on mating parts.
Use base part to which other components are added.
Use modular design-
Each sub-assembly should consists of 5-15 parts
Easier maintenance and field service
Facilitates automated assembly
Reduces inventory requirement
Reduces final assembly time
Avoid threaded fasteners.
Use fast assembly technique such as snap fits and adhesive bonding.
Minimum no. of distinct fasteners.