## Slide 1
Sharad Institute of Technology, College of Engineering, Yadrav.
Department of Mechanical Engineering.
APPLIED THERMODYNAMICS
BOILERS (UNIT 3)

## Slide 2: Boilers

## Slide 3: Boilers
Boiler is an apparatus to produce steam. Thermal energy released by combustion of fuel is used to make steam at the desired temperature and pressure.
The steam produced is used for:
(i) Producing mechanical work by expanding it in steam engine or steam turbine.
(ii) Heating the residential and industrial buildings
(iii) Performing certain processes in the sugar mills, chemical and textile industries.

## Slide 4
Boiler properties:
(i) Safety. The boiler should be safe under operating conditions.
(ii) Accessibility. The various parts of the boiler should be accessible for repair and maintenance.
(iii) Capacity. Should be capable of supplying steam according to the requirements.

## Slide 5
(iv) Efficiency. Should be able to absorb a maximum amount of heat produced due to burning of fuel in the furnace.
(v) It should be simple in construction .
(vi) Its initial cost and maintenance cost should be low.
(vii) The boiler should have no joints exposed to flames.
(viii) Should be capable of quick starting and loading.

## Slide 6: CLASSIFICATION OF BOILERS
According to what flows in the TUBE
1. Water tube.
2. Fire tube.

## Slide 7
Fire – tube Boilers

## Slide 9: Water tube boilers

## Slide 10: BABCOCK WILCOX BOILER

## Slide 11: MERITS OF WATER TUBE BOILERS OVERFIRE TUBE BOILERS
1. Generation of steam is much quicker due to small ratio of water content to steam content. This also helps in reaching the steaming temperature in short time.
2. Its evaporative capacity is considerably larger and the steam pressure range is also high-200 bar.
3. Heating surfaces are more effective as the hot gases travel at right angles to the direction of water flow.

## Slide 12
4. The combustion efficiency is higher because complete combustion of fuel is possible as the combustion space is much larger.
5. The thermal stresses in the boiler parts are less as different parts of the boiler remain at uniform temperature due to quick circulation of water.
6. The boiler can be easily transported and erected as its different parts can be separated.

## Slide 13
7. Damage due to the bursting of water tube is less serious. Therefore, water tube boilers are sometimes called safety boilers.
8. All parts of the water tube boilers are easily accessible for cleaning, inspecting and repairing.
9. The water tube boiler's furnace area can be easily altered to meet the fuel requirements.

## Slide 14: Demerits :
1. It is less suitable for impure and sedimentary water, as a small deposit of scale may cause the overheating and bursting of tube. Therefore, use of pure feed water is essential.
2. They require careful attention. The maintenance costs are higher.
3. Failure in feed water supply even for short period is liable to make the boiler over-heated.

## Slide 15: advantages of fire tube boilers are as follows.
(i) Low cost
(ii) Fluctuations of steam demand can be met easily
(iii) It is compact in size.

## Slide 16: Water tube boilers are classified as
1. Horizontal straight tube boilers
(a) Longitudinal drum (b) Cross-drum.
2. Bent tube boilers
(a) Two pass (b) Three pass
3. Cyclone fired boilers

## Slide 17
Fire – tube Boilers
Cochran Boiler

## Slide 18
Cochran Boiler
Fire – tube Boilers

## Slide 19
The outstanding features of this boiler are :
  It is very compact and requires minimum floor area
  Any type of fuel can be used with this boiler
  Well suited for small capacity requirements
  It gives about 70% thermal efficiency with coal firing and about 75% with oil firing

## Slide 20
Fusible Plug.
If the water level in the boiler falls below a predetermined level, the boiler shell and tubes will be overheated.
Main parts ……

## Slide 22
Water Level Indicator.
This indicates the water level in the boiler .

## Slide 24
Pressure Gauge.
This indicates the pressure of the steam in the boiler.

## Slide 26
Steam Stop Valve.
It regulates the flow of steam supply outside. The steam from the boiler first enters into an ant-priming pipe where most of the water particles associated with steam are removed

## Slide 28
Safety Valve.
The function of the safety valve is to prevent the increase of steam pressure in the holler above its design pressure.

## Slide 30
Feed Check Valve.
The high pressure feed water is supplied to the boiler through this valve. This valve opens towards the boiler only and feeds the water to the boiler.

## Slide 32
Blow-off Cock.
The water supplied to the boiler always contains impurities like mud, sand and, salt Due to heating, these are deposited at the bottom of the boiler, they have to be removed using blow off cock.

## Slide 34
Air Pre-heater

## Slide 36
LOCOMOTIVE BOILER

## Slide 37: Advantages
1. Large rate of steam generation per square metre of heating surface. To some extent this is due to the vibration caused by the motion.
2. It is free from brickwork, special foundation and chimney. This reduces the cost of installation.
3. It is very compact.
The pressure of the steam is limited to about 20 bar.

## Slide 39: Features
1. The evaporative capacity of this boilers is high compared with other boilers (20,000 to 40,000kg/hr). The operating pressure lies between 11.5 to 17.5 bar.
2. The draught loss is minimum compared with other boilers.
3. The defective tubes can be replaced easily.
4. The entire boiler rests over an iron structure, independent of brick work, so that the boiler may expand or contract freely. The brick walls which form the surroundings of the boiler are only to enclose the furnace and the hot gases.

## Slide 40: Boiler performance
1) Evaporative capacity
can be expressed in terms of:
a) kg of steam/hr
b) kg of hour/hr/m2 of heating surface
c) kg of steam/kg of fuel fired

## Slide 41: Boiler efficiency
Ratio of heat actually utilized in the generator to the heat supplied by the fuel.
Efficiency= mw(h-hf)/C
Where C is the calorific value

## Slide 42: BOILER MOUNTINGS

## Slide 43: BOILER MOUNTINGS
WATER LEVEL INDICATOR (Dec 05, Dec 08)
Notes: <number>

## Slide 44: BOILER MOUNTINGS
2. PRESSURE GAUGE (Bourdon’s) (Dec 05)
Records gauge pressure
Elliptical spring tube is also called Bourdon tube and is made up of special quality Bronze.
Plug (P) is provided for cleaning the siphon tube.
Siphon is filled with cold water to prevent the hot steam entering into the bourdon tube and spring tube remains comparatively cool.

## Slide 45: SAFETY VALVES
LEVER SAFETY VALVE
Dead Weight safety valve

## Slide 46: SAFETY VALVES
SPRING LOADED SAFETY VALVE
HIGH STEAM AND LOW WATER SAFETY VALVE

## Slide 47
JUNCTION VALVE:
The valve placed directly on a boiler in order to regulate the steam supply from boiler to steam pipe is called the Junction Valve.
STOP VALVE:
The valve used to regulate the steam supply from the steam pipe to the prime mover (steam engine or steam turbine) is called Stop Valve.

## Slide 48: JUNCTION VALVE

## Slide 49: FEED CHECK VALVE
Feed check valve works as NRV (Non- return valve). Prevents the back flow of water from the boiler when the feed water pump is either not working or in case of its failure.

## Slide 50: BLOW-OFF COCK

## Slide 51: FUSIBLE PLUG
Plugs P and R are made up of Gun Metal.
Plug S is made up of Copper.
Plug R is screwed to the plug P.
Plug S is locked into plug R by a metal like tin or lead.

## Slide 52: MANHOLE
This is provided at suitable position on the boiler shell so that the man can enter into boiler shell for inspection, maintenance and repairs. This hole is usually made in elliptical shape of the size convenient for a man to enter through this hole. The opening is closed by steam tight cover.

## Slide 53: STEAM TRAP
Steam trap is used to collect and automatically drain away the water resulted from partial condensation of steam without steam to escape with this condensate through a valve. The valve after draining the condensate is closed. Is presses the leakage of steam from the trap.
,

## Slide 54: ANTIPRIMING PIPE
It is attached below the stop valve to avoid the water particles being carried away along with steam. It has closed pipe with closed ends of 1m and 2m length. The top side of the pipe has perforations. When the steam passes through it, due to inertia effect, the moisture of steam falls into the pipe and the steam with reduced moisture passes into the stop valve.

## Slide 55: BOILER ACESSORIES
The devices used to improve the performance and operation of the boilers are called boiler accessories. Main accessories used are:
(UPTU-Dec 04,Dec 05)

## Slide 56: BOILER ACCESSORIES
WATER HEATING DEVICES
(UPTU- Dec 05)
Used to heat the feed water before it is fed to boiler with the help of steam of a steam engine.
Heating of feed water can be carried out either by:
Open Heater- Direct mixing
Closed heater- Indirect convection
WATER FEEDING DEVICES Used to supply water while the boiler is in operation. These devices include the use of feed pumps either reciprocating type or centrifugal type.

## Slide 57: INJECTOR (UPTU-Dec 04, Dec 05, Dec o6)

## Slide 58: SUPER HEATERS (UPTU-Dec 04, Dec 05, Dec 06)

## Slide 59: ECONOMISER

## Slide 60: AIR PREHEATER (UPTU- Dec 05)