## Slide 1
Sharad Institute of Technology, College of Engineering, Yadrav.
Department of Mechanical Engineering.
APPLIED THERMODYNAMICS
STEAM TURBINE (UNIT 5,6)

## Slide 2
To study and understand the process of steam flow in impulse and reaction turbine.
To visualize the following for impulse steam turbine.
  Steam flow
  Expansion of steam in LP and HP stages
Notes: <number>

## Slide 3
A steam turbine is a thermo-mechanical device that extracts thermal energy from pressurized steam, and converts it into rotary motion.
Steam turbine
Notes: <number>
Voice Over
A steam turbine is a mechanical device that extracts thermal energy from pressurized steam, and converts it into rotary motion.
<number>

## Slide 4
Steam
Steam is vapourized water. It is a transparent gas. At standard temperature and pressure, pure steam (unmixed with air, but in equilibrium with liquid water) occupies about 1,600 times the volume of an equal mass of liquid water.
Saturated steam is steam at equilibrium with liquid water at the same pressure and temperature.
Superheated steam is steam at a temperature higher than its boiling point at a given pressure
Notes: <number>
Steam is vapourized water. It is a transparent gas. At standard temperature and pressure, pure steam (unmixed with air, but in equilibrium with liquid water) occupies about 1,600 times the volume of an equal mass of liquid water.
Saturated steam is steam at equilibrium with liquid water.
Superheated steam is steam at a temperature higher than its boiling point at a given pressure
<number>

## Slide 5
Rankine Cycle
There are four processes in the Rankine cycle, these states are identified by number in the diagram to the right.
Process 1-2: The working fluid is pumped from low to high pressure, as the fluid is a liquid at this stage the pump requires little input energy.
Process 2-3: The high pressure liquid enters a boiler where it is heated at constant pressure by an external heat source to become dry saturated vapour.
Process 3-4: The dry saturated vapour expands through a turbine, generating power. This decreases the temperature and pressure of the vapour, and some condensation may occur.
Process 4-1: The wet vapour then enters a condenser where it is condensed at a constant pressure and temperature to become a saturated liquid. The pressure and temperature of the condenser is fixed by the temperature of the cooling coils as the fluid is undergoing a phase-change.
Notes: <number>
Voice Over
There are four processes in the Rankine cycle, these states are identified by number in the diagram to the right.
Process 1-2: The working fluid is pumped from low to high pressure, as the fluid is a liquid at this stage the pump requires little input energy.
Process 2-3: The high pressure liquid enters a boiler where it is heated at constant pressure by an external heat source to become a dry saturated vapour.
Process 3-4: The dry saturated vapour expands through a turbine, generating power. This decreases the temperature and pressure of the vapour, and some condensation may occur.
Process 4-1: The wet vapour then enters a condenser where it is condensed at a constant pressure and temperature to become a saturated liquid. The pressure and temperature of the condenser is fixed by the temperature of the cooling coils as the fluid is undergoing a phase-change.
<number>

## Slide 6
T- s Diagram
Notes: <number>

## Slide 7
Impulse & Reaction turbines
An impulse turbine has fixed nozzles that orient the steam flow into high speed jets.
These jets contain significant kinetic energy, which the rotor blades, shaped like buckets, convert into shaft rotation as the steam jet changes direction.
A pressure drop occurs across only the stationary blades, with a net increase in steam velocity across the stage.
Notes: <number>
Voice Over
An impulse turbine has fixed nozzles that orient the steam flow into high speed jets.
These jets contain significant kinetic energy, which the rotor blades, shaped like buckets, convert into shaft rotation as the steam jet changes direction.
A pressure drop occurs across only the stationary blades, with a net increase in steam velocity across the stage.
<number>

## Slide 8
Reaction turbine
In the reaction turbine, the rotor blades themselves are arranged to form convergent nozzles.
This type of turbine also makes use of the reaction force produced as the steam accelerates through the nozzles formed by the rotor.
Steam is directed onto the rotor by the fixed vanes of the stator. It leaves the stator as a jet that fills the entire circumference of the rotor.
The steam then changes direction and increases its speed relative to the speed of the blades.
A pressure drop occurs across both the stator and the rotor, with steam accelerating through the stator and decelerating through the rotor, with no net change in steam velocity across the stage but with a decrease in both pressure and temperature, reflecting the work performed in the driving of the rotor.
Notes: <number>
Voice Over
In the reaction turbine, the rotor blades themselves are arranged to form convergent nozzles.
This type of turbine makes use of the reaction force produced as the steam accelerates through the nozzles formed by the rotor.
Steam is directed onto the rotor by the fixed vanes of the stator. It leaves the stator as a jet that fills the entire circumference of the rotor.
The steam then changes direction and increases its speed relative to the speed of the blades.
A pressure drop occurs across both the stator and the rotor, with steam accelerating through the stator and decelerating through the rotor, with no net change in steam velocity across the stage but with a decrease in both pressure and temperature, reflecting the work performed in the driving of the rotor.
<number>

## Slide 9
Working of steam turbine based power plant
Notes: <number>

## Slide 10
Working
Steam is generated in steam generator and supplied to steam turbine at high pressure. (Usually sub critical pressure)
This steam enters the high pressure rotor and expands , to produce work.
Low pressure turbine stage is provided to extract more amount of work from the steam leaving into the condenser.
Notes: <number>
Voice Over
Steam is generated in Steam generator and supplied to steam turbine at high pressure. (Usually Sub critical pressure)
This steam enters the High pressure rotor and expands , to produce work.
low pressure turbine stage is provided to extract more amount of work from the steam leaving into the condenser.
<number>

## Slide 11
Steam turbine Blades
Steam turbine blades are subjected to high thermal stresses.
They are made of Ni-chrome steel.
Notes: <number>
Voice Over
Steam turbine blades are subjected to high thermal stresses.
They are made of Ni-chrome steel.
<number>

## Slide 12
Stator & Rotor
Steam enters in the stator and then enters into the rotor.
The pressure drop occurs in stator for impulse turbines where as for reaction turbines pressure drop occurs in both stator and rotor.
Work is produced in the rotor by the steam because of a reduction in its pressure(reaction turbine) and a change in the direction of its velocity (reaction and impulse turbines).
Notes: <number>
Voice Over
Steam Enters in the stator and then enters into the rotor.
The pressure drop occurs in stator for Impulse turbines where as for reaction turbines pressure drop occurs in both stator and rotor.
Work is produced in the rotor by the high pressure steam expanding in the lower stages of the turbine.
<number>

## Slide 13
Steam enters axially and leaves axially. (generally in axial-flow steam turbines)
Velocity triangles
Notes: <number>
Voice Over
Steam enters axially and leaves axially .
<number>

## Slide 14
U
Vri
Vre
U
Vri
Vai
Inlet Velocity Triangle
Exit Velocity Triangle
U
Vre
Vae
The velocity of the fluid approaching the bucket = Vai . The velocity of the bucket = U. The velocity of the approaching fluid to relative the bucket velocity is Vri = Vai - U The velocity of the outlet fluid relative the bucket velocity is Vre =k(Vri)
(k being a friction loss factor) The velocity of the fluid in the direction of bucket movement -> is the whirl velocity.
The outlet whirl velocity Vae is simply given by, Vae = U - Vre(cos (π - θ)
Notes: <number>

## Slide 15
Work Done / kg of steam
Work done / kg of steam is called specific work out put of turbine.
W.D/kg = U * (Vai + Vae)
U = Blade Velocity
Vai= Whirl velocity at inlet
Vae= Whirl velocity at outlet
Power output = Ms *[U * (Vai + Vae)]
Ms = Mass flow rate of steam in kg/s = [ ρ * Q ]
Where ρ = density (kg/m3) and Q = Volume flow rate (m3 /s).
Notes: <number>
Voice Over
Work done / Kg of steam is called specific work out put of turbine.
W.D/Kg = Cb * (Cw1+Cw2)
Cb = Blade Velocity
Cw1= Whirl velocity at inlet
Cw2= Whirl velocity at outlet
Power output = Ms *[Cb * (Cw1+Cw2)]
Ms = Mass flow rate of steam in Kg/sec
<number>

## Slide 16
User interface For simulation of Steam turbine
Notes: <number>

## Slide 17
Operation 1
Notes: <number>

## Slide 18
Operation 2
Reference : http://atd.na.amec.com/flash_power.html
Notes: <number>

## Slide 19
Operation 3
Notes: <number>

## Slide 20
Refer excel sheet for calculations
Notes: <number>

## Slide 21
Pressure drop occurs in which part in reaction turbine
Stator only
Rotor only
Stator and Rotor
Nozzles and Rotor
Notes: <number>

## Slide 22
If shaft rotates in clockwise sense in reaction turbine then casing will rotate in
same direction
Does not rotate
Opposite direction
Both clock and counter clock direction.
Notes: <number>

## Slide 23
Steam flow in impulse steam Turbine is as follows
Expands in nozzle, expands in stator, expands in rotor and leaves the system.
Expands in nozzle, expands in stator, pressure drop remains constant in rotor and leaves the system.
Expands in Stator and does not expand in rotor assembly.
Expands in rotor and does not expands in stator.
Notes: <number>

## Slide 24
References
Reference links:
http://atd.na.amec.com/flash_power.html
http://www.cf.missouri.edu/energy/em_fun/flash/turbine.swf
http://web.iitd.ac.in/~pmvs/jgl710/jgl710-26.ppt
http://www.roymech.co.uk/Related/Fluids/Fluids_Machines.html
Books:
Turbomachines by R. Yadav
Fans compressors and turbines by SM Yahya
Notes: <number>