## Slide 1: LESSON 21: MATERIAL REQUIREMENTS PLANNING
Outline
Hierarchy of Production Decisions
MRP and its importance
Input and Output of an MRP system
MRP Calculation
Lot Sizing
Lot Sizing with Capacity Constraint

## Slide 2
The next slide presents a schematic view of the aggregate production planning function and its place in the hierarchy of the production planning decisions.
Forecasting: First, a firm must forecast demand for aggregate sales over the planning horizon.
Aggregate planning: The forecasts provide inputs for determining aggregate production and workforce levels over the planning horizon.
Master production schedule (MPS): Recall, that the aggregate production plan does not consider any “real” product but a “fictitious” aggregate product. The MPS translates the aggregate plan output in terms of specific production goals by product and time period. For example,
Hierarchy of Production Decisions

## Slide 3
Hierarchy of Production Decisions

## Slide 4
suppose that a firm produces three types of chairs: ladder-back chair, kitchen chair and desk chair. The aggregate production considers a fictitious aggregate unit of chair and find that the firm should produce 550 units of chairs in April. The MPS then translates this output in terms of three product types and four work-weeks in April. The MPS suggests that the firm produce 200 units of desk chairs in Week 1, 150 units of ladder-back chair in Week 2, and 200 units of kitchen chairs in Week 3.
Material Requirements Planning (MRP): A product is manufactured from some components or subassemblies. For example a chair may require two back legs, two front legs, 4 leg supports, etc. While forecasting, aggregate plan
Hierarchy of Production Decisions

## Slide 5: Hierarchy of Production Decisions Master Production Schedule
Ladder-back chair
Kitchen chair
Desk chair
1
2
April
May
790
3
4
5
6
7
8
200
150
120
200
150
200
120
Aggregate
production plan
for chair family
550
200
Notes: <footer>
<header>
<date/time>
Aggregate production plan - 550 units in April, 790 units in May
Master production schedule translate 550 chairs in April into various types of chairs in various weeks of April, 790 chairs in May into various types of chairs in various weeks of May.

## Slide 6
and MPS consider the volume of finished products, MRP plans for the components, and subassemblies. A firm may obtain the components by in-house production or purchasing. MRP prepares a plan of in-house production or purchasing requirements of components and subassemblies.
Scheduling: Scheduling allocates resource over times in order to produce the products. The resources include workers, machines and tools.
Vehicle Routing: After the products are produced, the firm may deliver the products to some other manufacturers, or warehouses. The vehicle routing allocates vehicles and prepares a route for each vehicle.
Hierarchy of Production Decisions

## Slide 7: Hierarchy of Production Decisions Materials Requirement Planning
Back slats
Leg supports
Seat cushion
Seat-frame
boards
Front
legs
Back
legs
Notes: <footer>
<header>
<date/time>

## Slide 8
Material Requirements Planning
The demands for the finished goods are obtained from forecasting. These demands are called independent demand.
The demands for the components or subassemblies depend on those for the finished goods. These demands are called dependent demand.
Material Requirements Planning (MRP) is used for dependent demand and for both assembly and manufacturing
If the finished product is composed of many components, MRP can be used to optimize the inventory costs.

## Slide 9
Next two slides explain the importance of an MRP system. The first one shows inventory levels when an MRP system is not used. The next one shows the same when an MRP system is used.
The chart at the top shows inventory levels of the finished goods and the chart on the bottom shows the same of the components.
If the production is stopped (like it is at the beginning of the chart), the finished goods inventory level decreases because of sales. However, the component inventory level remains unchanged. When the production resumes, the finished goods inventory level increases, but the component inventory level decreases.
Importance of an MRP System

## Slide 10
Inventory without an MRP System
Importance of an MRP System

## Slide 11
Inventory with an MRP System
Importance of an MRP System

## Slide 12
Without an MRP system:
  Component is ordered at time A, when the inventory level of the component hits reorder point, R
  So, the component is received at time B.
  However, the component is actually needed at time C, not B. So, the inventory holding cost incurred between time B and C is a wastage.
With an MRP system:
  We shall see in this lesson that given the production schedule of the finished goods and some other information (see the next slide), it is possible to predict the exact time, C when the component will be required. Order is placed carefully so that it is received at time C.
Importance of an MRP System

## Slide 13
MRP Inputs:
  Master Production Schedule (MPS): The MPS of the finished product provides information on the net requirement of the finished product over time.
  Bill of Materials: For each component, the bill of materials provides information on the number of units required, source of the component (purchase/ manufacture), etc. There are two forms of the bill of materials:
    Product Structure Tree: The finished product is shown at the top, at level 0. The components assembled to produce the finished product is shown at level 1 or below. The sub-components used to produce the components at level 1 is
MRP Input and Output

## Slide 14
MRP
computer
program
Bill of
Materials
file
Inventory
file
Master
Production
Schedule
Reports
To Production
To Purchasing
Forecasts
Orders
MRP Input and Output

## Slide 15
    shown at level 2 or below, and so on.
    The number in the parentheses shows the requirement of the item. For example, “G(4)” implies that 4 units of G is required to produce 1 unit of B.
    The levels are important. The net requirements of the components are computed from the low levels to high. First, the net requirements of the components at level 1 is computed, then level 2, and so on.
MRP Input and Output

## Slide 16
    Bill of Materials: For each item, the name, number, source, and lead time of every component required is shown on the bill of materials in a tabular form.
  Inventory file: For each item, the number of units on hand is obtained from the inventory file.
MRP Output:
  Every required item is either produced or purchased. So, the report is sent to production or purchasing.
MRP Input and Output

## Slide 17
Bill of Materials: Product Structure Tree
Level 1
Level 0
Level 2
Level 3

## Slide 18
Bill of Materials

## Slide 19
Bill of Materials

## Slide 20
Component Units in Lead
Inventory time
(weeks)
Seat
Subassembly 25 2
Seat frame 50 3
Seat frame
boards 75 1
On Hand Inventory and Lead time

## Slide 21
Now, the MRP calculation will be demonstrated with an example.
Suppose that 150 units of ladder-back chair is required.
The previous slide shows a product structure tree with seat subassembly, seat frames, and seat frame boards. For each of the above components, the previous slide also shows the number of units on hand.
The net requirement is computed from top to bottom. Since 150 units of ladder-back chair is required, and since 1 unit of seat subassembly is required for each unit of ladder-back chair, the gross requirement of seat-subassembly is 1501 =150 units. Since there are 25 units of seat-subassembly in the inventory, the net requirement of the seat-subassembly is 150-25 = 125
MRP Calculation

## Slide 22
units. Since 1 unit of seat frames is required for each unit of seat subassembly, the gross requirement of the seat frames is 1251 = 125 units. (Note that although it follows from the product structure tree that 1 unit of seat frames is required for each unit of ladder-back chair, the gross requirement of seat frames is not 150 units because each of the 25 units of seat-subassembly also contains 1 unit of seat frames.) Since there are 50 units of seat frames in the inventory, the net requirement of the seat frames is 125-50 = 75 units. The detail computation is shown in the next two slides.
A similar logic is used to compute the time of order placement.
MRP Calculation

## Slide 23
MRP Calculation
Assume that 150 units of ladder-back chairs are to be produced at the end of week 15

## Slide 24
Assume that 150 units of ladder-back chairs are to be produced at the end of week 15 and that there is a one-week lead time for ladder-back chair assembly
MRP Calculation: Time of Order Placement

## Slide 25
Scheduled Receipts:
  Items ordered prior to the current planning period and/or
  Items returned from the customer
Lot-for-lot (L4L)
  Order quantity equals the net requirement
  Sometimes, lot-for-lot policy cannot be used. There may be restrictions on minimum order quantity or order quantity may be required to multiples of 50, 100 etc.
MRP Calculation: Some Definitions

## Slide 26
Example 1: Each unit of A is composed of one unit of B, two units of C, and one unit of D. C is composed of two units of D and three units of E. Items A, C, D, and E have on-hand inventories of 20, 10, 20, and 10 units, respectively. Item B has a scheduled receipt of 10 units in period 1, and C has a scheduled receipt of 50 units in Period 1. Lot-for-lot (L4L) is used for Items A and B. Item C requires a minimum lot size of 50 units. D and E are required to be purchased in multiples of 100 and 50, respectively. Lead times are one period for Items A, B, and C, and two periods for Items D and E. The gross requirements for A are 30 in Period 2, 30 in Period 5, and 40 in Period 8. Find the planned order releases for all items.
MRP Calculation

## Slide 27
Level 0
Level 1
Level 2
MRP Calculation

## Slide 28
MRP Calculation

## Slide 29
MRP Calculation
1
WK
L4L
30 30 40
20
All the information above are given.

## Slide 30
MRP Calculation
1
WK
L4L
30 30 40
--
20 20
20 units are just transferred from Period 1 to 2.

## Slide 31
MRP Calculation
1
WK
L4L
30 30 40
--
20 20
10
10
10
10
The net requirement of 30-20=10 units must be ordered in week 1.

## Slide 32
MRP Calculation
1
WK
L4L
30 30 40
--
20 20 0 0 0
10
10
10
10
On hand in week 3 is (20+10)-30=0 unit.

## Slide 33
MRP Calculation
1
WK
L4L
30 30 40
--
20 20 0 0 0
10
30
30
10
10
30
10
30
The net requirement of 30-0=30 units must be ordered in week 4.

## Slide 34
MRP Calculation
30 30 40
1
WK
L4L
--
20 20 0 0 0 0 0 0
10
30
40
30
40
10
10
30
40
10
30
40
The net requirement of 40-0=30 units must be ordered in week 7.

## Slide 35
MRP Calculation
30 30 40
1
WK
L4L
--
20 20 0 0 0 0 0 0 0 0
10
30
40
30
40
10
10
30
40
10
30
40
The net requirement of 40-0=30 units must be ordered in week 7.

## Slide 36
MRP Calculation
Exercise

## Slide 37
MRP Calculation
Exercise

## Slide 38
MRP Calculation
Exercise

## Slide 39
MRP Calculation
Exercise

## Slide 40
READING AND EXERCISES
Lesson 21
Reading:
Section 7.1 pp. 355-364 (4th Ed.), pp. 346-358 (5th Ed.)
Exercise:
4 and 9 pp. 364-366 (4th Ed.), pp. 356-358 (5th Ed.)