## Slide 1
Process Analysis
Operation Analysis
(Micro) Motion Study
Time Study
Work Instruction Establishing
Work Study
Notes: IM 313 Work Study
Issue 9: Motion Study
Copyright 2001 by Sajee Sirikrai
<number>

## Slide 2
Eliminate unnecessary operations
Ease the necessary operations
Balance the uses of body
Reduce cycle time
To improve Work Method

## Slide 3
Motion Study Techniques
Process Analysis
Operation Analysis
Motion Pictures (Stop-Action pictures)
Film Analysis
Fundamental Hand Motions (Therblig Analysis)
Principles of Motion Economy
Standard Job Conditions: Factory Act

## Slide 4
Film Analysis
Concept: Record movement of a working operator with an appropriate film technique, then list all observed motions and time employed into an analysis sheet
Film Production: Methods & equipment
Micromotion
Memomotion
Cyclegraphic
Chronocyclegraphic

## Slide 5
Film Analysis
The Analysis: Simultaneous motion cycle Chart ( SIMO chart )
Observer’s abilities
see motions made by the operator’s right and left hands
notice what the fingers of each hand do
detect where one motion ends and another begins
judge the lengths of motions
estimate times of the motions
Motion-minded

## Slide 6: SIMO Chart

## Slide 7
Fundamental Hand Motions :Therblig
Therblig: The system of symbols that represent every elementary of hand / arm and eye movements
Types of Therblig
1) Motions required for performing an operation
2) Motions that tend to slow down type 1 motion
3) Motions that do not perform an operation

## Slide 8
Transport empty
Grasp
Transport loaded (carry)
Position
Use
Assemble
Disassemble
Release load
Inspect
Type 1

## Slide 9
Search
Find*
Select
Plan (person thinking)
Pre-position (set up)
Type 2

## Slide 10
Hold
Unavoidable delay
Avoidable delay (standby)
Rest
Type 3

## Slide 11: Therblig Symbols

## Slide 12
Therblig Analysis Steps
Take time to carefully observe the overall operation
Try to picture the operation in your mind
Write down the steps in the operation, starting with just one hand’s motion
Re-observe the operation and correct the written description
Describe the motions in more detail and fill out the therblig symbols
Accurate
description

## Slide 13: Therblig Analysis Chart

## Slide 14
Micromotion Study: A Trial
6 Participants
12 IE
make 12 sets of invitation letter
Operation / Therblig chart
Workplace setting

## Slide 15
<number>
A Trial: What's up?

## Slide 16
As related to
Uses of the human body
Arrangement of the work place
Design of tools and equipment
Principles of Motion Economy
You need a good checklists

## Slide 17: Principles of Motion Economy As related to the uses of the human body
Two hands should begin and complete their motions at the same time.
Two hands should not be idle at the same time.
Motions of the arms should be made in opposite and symmetrical direction and should be made simultaneously.
Hand and body motions should be confined to the lowest classification with which it is possible to perform the work satisfactorily.

## Slide 18: Principles of Motion Economy As related to the uses of the human body
Momentum should be employed to assist the worker wherever possible, and it should be reduced to a minimum if it must be overcome by muscular effort.
Ballistic movement are faster, easier and more accurate than restricted or controlled movements.
Work should be arranged to permit an easy and natural rhythm wherever possible.
Eye fixations should be as few and as close as possible.

## Slide 19: Principles of Motion Economy As related to the workplace arrangement
There should be a definite and fixed place for all tools and materials.
Tools, materials and controls should be located close to the point of uses.
Gravity feed bins and containers should be used to deliver material close to the point of use.
Drop deliveries should be used wherever possible.
Materials and tools should be located to permit the best sequence of motions.

## Slide 20: Principles of Motion Economy As related to the workplace arrangement
Provisions should be made for adequate conditions for seeing. Good illumination is the first requirement for satisfactory visual perception.
The height of the work place and the chair should be preferably arranged so that alternate sitting and standing at work are easily possible.
A chair of the type and height to permit good posture should be provided for every worker.

## Slide 21: Principles of Motion Economy As related to the equipment design
The hands should be relieved of all work that can be done more advantageously by a jig, a fixture, or a foot-operated device.
Two or more tools should be combined whenever possible.
Tools and materials should be pre-positioned whenever possible.

## Slide 22: Principles of Motion Economy As related to the equipment design
Where each finger performs some specific movement, such as in typewriting, the load should be distributed in accordance with the inherent capacities of the fingers.
Levers, hand wheels, and other controls should be located in such positions that the operator can manipulate them with the least change in body position and with the greatest speed and ease.

## Slide 23: Therbilg Analysis Checkpoints

## Slide 24
Proposed Method Implementation
Cost - Benefit Ratio
Worker involvement in method change
Change Resistance
Hawthorne effect

## Slide 25
Cross functional Cooperation
Planning and Control
Maintenance
Quality Inspection
Laws and Regulations
Safety
Labor Relation
Quality/Productivity
Precautions

## Slide 26
Expenses & Benefit of Study
Extensiveness of task
Life of the task
Labor consideration
Investment
Economy of the Study