## Slide 1: Time and Motion Study
<number>
Rebecca Johnston
Operations Management
Dr. Foster
Notes: <number>

## Slide 2: Time and Motion Study: Defined
<number>
A method created to determine the ‘correct time’ it takes to complete a certain task
A method to establish ‘the one best way to perform a task’
Notes: <number>
Tine and Motion Study Defined:
All of the motions in a job need to be established so a sequence of motions can be determined to ensure that the task is being preformed in the most efficient and effective way.

## Slide 3: Time and Motion Study: Purposes
<number>
To end ‘goofing off’ and to establish what constituted a fair days work
To make sure that the job being evaluated does not include any unnecessary motion by the worker

## Slide 4: Time and Motion Study: History
<number>
Frederick W. Taylor and his followers developed and refined the Time Study
Frank B. Gilbreth and his wife Lillian developed and refined the Motion Study
Historically the two studies are discussed individually, today they generally are discussed as one

## Slide 5: Time and Motion Study: In your Organization
<number>
Historically: T&M Studies were used in the manufacturing industry to evolve pay scales with the thought that money was the only motivation for work
Notes: <number>
This idea, that people are only motivated by money, has been disproved. Things like job satisfaction and environment are more important to employees than pay.

## Slide 6: Time and Motion Study: In your Organization cont’d
<number>
Today:
  T&M Studies can be effective for performance evaluations
  T&M Studies can be used for planning purposes in order to predict the level of output that may be achieved
  T&M Studies can be used to uncover problems and create solutions
  T&M Studies can be used for time cost analysis
Notes: <number>
The effective cost of an employee, per unit of time for the task they are primarily responsible for.
The allocation of time to various ‘productive’ and ‘non-productive’ tasks.
Review of alternatives to make the best use of time.

## Slide 7: Time and Motion Study: Objective
<number>
The objective of the Time and Motion Study is to determine a ‘normal’ or average time for a job, by using observers to record exactly how much time is being devoted to each task.

## Slide 8: How it Works Step-by-Step
<number>
1. Establish the standard job method.
2. Break down the
job into elements
3. Study the job.
4. Rate the worker’s performance
Notes: <number>
Complete step one by analyze the job using methods analysis, this will allow you to be sure the best method is being used.
Complete step two by breaking the job down into short tasks with ‘break points’ in between.
Complete step three by conducting the actual timing of each job element with the traditional stopwatch attached to a clipboard or a hand held electronic time-study machine.
Complete step four by using a performance rating factor of 100 percent. 100 percent reflects a normal work performance, less than 100 percent means a below average performance, greater than 100 percent means better then a normal performance.

## Slide 9: How it Works Step-by-Step cont’d
<number>
5. Compute the average time
6. Compute the normal time
Nt=(t)(RF) or
Normal Time=(elemental average time)
(rating factor)
7. Compute the standard time
ST=(Nt)(1+AF) or
Standard Time=(Normal cycle time)(1+Allowance factor)
Notes: <number>
5. To complete step five a sufficient number of job cycles need to be observed, and then an average time.
6. After computations are made for the normal time, the normal cycle time needs to be computed before step 7. This is done by summing the elemental normal times. The directions for finding the rating factor can be found in step 4.
7. An allowance factor is inserted into the formula for work delays like mechanical breakdowns, personal delays, and normal fatigue.

## Slide 10: Time and Motion Study: In Action
<number>
How do medical residents spend their time at the hospital?
Notes: <number>

## Slide 11: In Action cont’d
<number>
1. Coders/observers training was the
2. Activities were broken down into separate categories, 67 in total
3. The exact number of minutes per task were determined
4. Percentages of time devoted to each task were calculated
Notes: <number>
In 1992 a study was conducted to determine how residents in hospitals spend their time on rounds.
To do this the time and motion study used 22 coders, undergraduate pre-med students. They each received seven hours of training before the study began.
The data included information from 2 interns and 3 residents at Bellevue Hospital in New York, 2 interns and 1 resident at New York University Medical Center out of roughly 600 interns/residents.
The coders measured the activities that were preformed and the time spent on each of them.

## Slide 12: In Action cont’d
<number>
A total of 13,383 minutes of activities were observed between the 8 residents
Residents were involved in 1,726 coded activities
These activities averaged 7.75 minutes each with a standard deviation of 14.5 minutes
Notes: <number>
Residents and interns are both called residents.
This use of a time and motion study has allowed the observers to see how residents time was allocated in hopes of improving their use of time.

## Slide 13: Time and Motion Study: Exercise
<number>
Element | t (min) | RF
1 | 2.51 | 1.10
2 | 5.29 | 1.15
3 | 4.21 | 1.10
4 | 3.57 | 1.05
Compute the standard time for this job using an allowance factor of 20 percent.

## Slide 14: Solution
<number>
Use the formula
(t)(RF)=Nt
Element 1
(.251)(1.10)=.2761
Element 2
(.529)(1.15)=.6084
And so on for element 3 and 4
Element | T(min) | RF | t | Nt
1 | 2.51 | 1.10 | .251 | .2761
2 | 5.29 | 1.15 | .529 | .6084
3 | 4.21 | 1.10 | .421 | .4631
4 | 3.57 | 1.05 | .357 | .3749
To get the normal cycle time you sum the Nt values. Here = 1.73 min

## Slide 15: Solution
<number>
To compute the standard time use the 20 percent allowance factor
Nt(1+AF)=ST
Here
1.73(1+.20)=2.08
So the standard time for each element of this job is 2.08 minutes

## Slide 16: Time and Motion Study: Problems
<number>
Observers are not always competent
Those conducting the study are not always proficient in the job being observed
The actions observed are not always reflective of the group as a whole
Notes: <number>
Observers must be competent, they must determine the difficulty of the job and decide what ‘normal’ performance is. An incompetent person will not be effective
Those conducting the study must be familiar with the job otherwise they will have no idea what they are watching for during the study.
Those that are observed may not be a good sample of the group as a whole, they may perform better or worse than the rest of the group

## Slide 17: Time and Motion Study: Problems cont’d
<number>
Workers may not cooperate with a time and motion study:
They may resent the study if it is being used to determine the pay scale
Workers may change the rate at which they work
Pressure may increase mistakes made
Workers may alter normal work methods to disrupt the study

## Slide 18: References
<number>
Ferguson, David S., Don’t Call it “time and motion study”, IIT Solutions, Norcross. May 1997. Vol. 29, Issue 5.
Finkler, Steven A., A Comparison of work-sampling and time-and-motion techniques for studies in health services research, Health Service Research, Chicago. Dec 1993. Vol. 28, Issue 5.
Koehler, Kenneth G., Time Cost Analysis, CMA, Hamilton. May 1992. Vol. 66, Issue 4.
Russell, Roberta; Taylor, Bernard W., Operations Management, Prentice Hall Inc., Upper Saddle River, NJ. 2000.
Stevens, Larry, Time Study Prompts New HR Efficiencies, Personnel Journal, Santa Monica. April 1994. Vol. 73, Issue 4.
Stuttaford, Genevieve, The One Best Way: Fredrick Winslow Taylor & the Enigma of Efficiency, Publishers Weekly, New York. March 17, 1997. Vol. 224, Issue 11.