## Slide 1: UNIT- I LINEAR MEASUREMENTS, TOLERANCES AND GAUGING

## Slide 2: Metrology. Metrology defines as the Science of pure measurement. But in engineering purposes, it in restricted to measurements of length and angles and other qualities which are expressed in linear or angular terms.

## Slide 3: Units and Standards
Units of Measurement:
C.G.S. System of Units
Centimeter – Gram – Second system of unit
M.K.S. System of Units:
Meter – kilogram – second system of units
International System (SI) of Units:
the meter (m), kilogram (k), second (s), and ampere (A) of the MKSA system and, in addition, the Kelvin (K) and the candela (cd) as the units of temperature and luminous

## Slide 4: Terminology in instrumentation
Precision  Degree of repetitiveness. If an instrument is not precise it will give different results for the same dimension for the repeated readings.
Accuracy  The maximum amount by which the result differ from true value(ie) Closeness to true value
Sensitivity
It is ratio between output signal to input signal.

## Slide 5
Readability is a measure of an instrument's ability to display incremental changes in its output value.
True size  Theoretical size of a dimension which is free from errors.
Actual size  size obtained through measurement with permissible error

## Slide 6
Repeatability is the variation in measurements taken by a single person or instrument on the same item and under the same conditions. A measurement may be said to be repeatable when this variation is smaller than some agreed limit.
Reproducibility is one of the main principles of the scientific method, and refers to the ability of a test or experiment to be accurately reproduced, or replicated, by someone else working independently.

## Slide 7: Calibration
Calibration of a measuring instrument
It is the process of determining the values of the quantity being measured corresponding to a pre-established arbitrary scale.
Advantages of calibration:
  Optimizes resources.
  Assures consistency.
  Ensures measurements (and perhaps products) are compatible with those made elsewhere.
  Eliminate or reduce bias in the user's measurement system relative to the reference base.

## Slide 8
Methods of measurement.
1. Direct Method
2. Indirect Method
3. Comparison Method
4. Coincidence Method.
Classification of measuring instruments.
1. Angle measuring instruments
2. Length measuring instruments
3. Instruments for surface finish
4. Instruments for deviations.

## Slide 9: Sources of error
Controllable Errors-
Calibration Errors ,ambient Conditions , Stylus pressure, avoidable errors
Random Errors
These occur randomly and the specific causes of such errors cannot be determined, but likely sources of this type of error are small variations in the position of setting standards and work piece, slight displacement of lever joints in the measuring joints in the measuring instrument,

## Slide 10
Parallax Error :
On most dials the indicating finger or pointer lies in a plane parallel to the scale but displaced a small distance away to allow free movement of the pointer. It is then essential to observe the pointer along a line normal to the scale otherwise a reading error will occur.

## Slide 11: Imperial Standard Yard
In practice, the accurate measurement must be made by comparison with a standard of known dimension and such a standard is called “Primary Standard”.
The first accurate standard was made in England and was known as “Imperial Standard yard”

## Slide 12: Imperial Standard Yard
1 yard = 0.9144 meter.

## Slide 13: Imperial Standard Yard
An imperial standard yard, shown in fig, is a bronze (82% Cu, 13% tin, 5% Zinc) bar of 1 inch square section and 38 inches long.
A round recess, 1 inch away from the two ends is cut at both ends up to the central or ‘neutral plane’ of the bar.
Further, a small round recess of (1/10) inch in diameter is made below the center.
Two gold plugs of (1/10) inch diameter having engravings are inserted into these holes so that the lines (engravings) are in neutral plane.
Yard is defined as the distance between the two central transverse lines of the gold plug at 620F.

## Slide 14: International Standard Meter

## Slide 15: International Standard Meter
This standard was established originally by International bureau of weights & Measures in year 1875.
The upper surface of the web is highly polished & the graduations are engraved on the upper surface of the web which coincides with the neutral axis of the section.
According to this standard the length of meter is defined as the straight line distance, at 0oC, between the engraved lines of pure platinum-iridium alloy (90% platinum & 10% iridium) of 1020 mm total length and having a ‘WEB’ cross section as shown in fig.

## Slide 16: Light (Optical) Wave Length Standard
Because of the problems of variation in length of material length standards, the possibility of using light as a basic unit to define primary standard has been considered.
The wavelength of a selected radiation of light and is used as the basic unit of length.
Since the wavelength is not a physical one, it need not be preserved & can be easily reproducible without considerable error.

## Slide 17: Light (Optical) Wave Length Standard
In 1907 the international Angstrom (Ao) unit was defined in terms of wavelength of red cadmium in dry air at 15 degree C.
According to this standard meter was defined as equal to 1650763.73 wavelengths of the red orange radiation of Krypton 86 gas.
1 meter = 1650763.73 wavelengths.

## Slide 18: Advantages of using wave length standards
1. Length does not change.
2. It can be easily reproduced if destroyed.
3. This primary unit is easily accessible to any physical laboratories.
4. It can be used for making measurements with much higher accuracy than material standards.
5. Wavelength standard can be reproduced consistently at any time and at any place.

## Slide 19: Line and End standard measurements
Line standard
Length is expressed as the distance between two lines.
End standard
Length is expressed as the distance between two flat parallel faces.
These are more accurate.
These requires more time for measurement.

## Slide 20
Slip Gauges
Slip gauges are rectangular blocks of high grade steel with exceptionally close tolerances. These blocks are suitably hardened though out to ensure maximum resistance to wear. They are then stabilized by heating and cooling successively in stages so that hardening stresses are removed.
The cross sections of these gauges are 9mm X 30mm for sizes up to 10mm and 9mm X 35mm for larger sizes.

## Slide 21: Slip gauges are used for
To get the high accuracy
For checking the accuracy of Vernier caliper, micrometer and such other measuring instruments.
For measure the angle of work piece with a sine bar.
Setting up a comparator to specific dimension.
To check gap between parallel locations such as in gap gauges or between two mating parts.

## Slide 22: Wringing of slip gauges
The success of precision measurement by slip gauges depends on the phenomenon of wringing. The slip gauges are wrung together by hand through a combined sliding and twisting motion. The gap between two wrung slips is only of the order of 0.00635 micron, which is negligible.

## Slide 23: Care of slip gauges
protect from dust, dirt and moisture.
Avoid magnetization.
Handle lapped faces as little as possible to prevent etching from finger acid. Remove all finger marks as soon as possible.
Wipe faces immediately before use even when use is continues.
Always replace clean gauges in their box and close the lid after use. If gauges are not frequently use, they should be coated with grease to prevent corrosion.
Do not handle gauges above the open box, they may cause damage to other gauges if dropped.

## Slide 24: Why study Limits & Fits?
Exact size is impossible to achieve.
Establish boundaries within which deviation from perfect form is allowed.
Enable interchangeability of components during assembly.
Limits : The maximum and minimum permissible sizes within which the actual size of a component lies are called Limits.
Tolerance: It is impossible to make anything to an exact size, therefore it is essential to allow a definite tolerance or permissible variation on every specified dimension.

## Slide 25: Terminology of limit systems
Zero Line: It is the line w.r.t which the positions of tolerance zones are shown.
Deviation: It is the algebraic difference between a limit of size and the corresponding basic size.
Upper Deviation: It is the algebraic difference between the maximum limit of size and the corresponding basic size. It is denoted by letters ‘ES’ for a hole and ‘es’ for a shaft.
Lower Deviation: It is the algebraic difference between the minimum limit of size and the corresponding basic size. It is denoted by letters ‘EI’ for a hole and ‘ei’ for a shaft.
Fundamental Deviation: It is the deviation, either upper or lower deviation, which is nearest to the zero line for either a hole or a shaft. It fixes the position of the tolerance zone in relation to the zero line.

## Slide 26: Terminology of limit systems

## Slide 27: Maximum and Minimum/Least Material Limits
Maximum Material Limit for Shaft is Upper Deviation
Minimum/Least Material Limit for Shaft is Lower Deviation
Maximum Material Limit for Hole is Lower Deviation
Minimum/Least Material Limit for Hole is Upper Deviation

## Slide 28: Unilateral tolerance and Bilateral tolerance

## Slide 29: SYSTEM OF FITS
Clearance fit: In this type of fit, the largest permitted shaft diameter is less than the smallest hole diameter so that the shaft can rotate or slide according to the purpose of the assembly.
  Loose Fit
  Running Fit
  Slide Fit

## Slide 30: SYSTEM OF FITS
Interference Fit
It is defined as the fit established when a negative clearance exists between the sizes of holes and the shaft
In this type of fit, the minimum permitted diameter of the shaft is larger than the maximum allowable diameter of the hole.
Ex: Bearing bushes, Keys & key ways, Ex: dowel pins, bearings in castings

## Slide 31: SYSTEM OF FITS
Interference Fit continued…
The smallest shaft is 1.2513” and the largest hole is 1.2506”, so that there is an actual interference of metal amounting to at least 0.0007”.
  Shrink fit or heavy force fit.
  Medium force fit.
  Tight fit or press fit.

## Slide 32: SYSTEM OF FITS
Transition Fit:
In this type of fit, the diameter of the largest allowable hole is greater than the smallest shaft, but the smallest hole is smaller than the largest shaft, such that a small positive or negative clearance exists between the shaft & hole.
Ex: Coupling rings, Spigot in mating holes, etc.

## Slide 33: SYSTEM OF FITS
Transition Fit:

## Slide 34: SYSTEM OF FITS

## Slide 35: SYSTEM OF FITS
Hole Basis System
In the hole basis system, the size of the hole is kept constant and shaft sizes are varied to obtain various types of fits.
In this system, lower deviation of hole is zero, i.e. the low limit of hole is same as basic size.
The hole basis system is commonly used because it is more convenient to make correct holes of fixed sizes, since the standard drills, taps, reamers and broaches etc. are available for producing holes and their sizes are not adjustable. On the other hand, size of the shaft produced by turning, grinding, etc. can be very easily varied.

## Slide 36: SYSTEM OF FITS
Shaft Basis System
In the shaft basis system, the size of the shaft is kept constant and different fits are obtained by varying the size of the hole.
The upper deviation (fundamental deviation) of shaft is zero, i.e. the high limit of the shaft is same as basic size.
Shaft basis system is used when the ground bars or drawn bars are readily available. These bars do not require further machining and fits are obtained by varying the sizes of the hole.

## Slide 37: SYSTEM OF FITS
Hole Basis System
Shaft Basis System

## Slide 38: Gauges
Gauges are inspection tool of rigid design, without a scale, which serves to check the dimensions of manufacturing parts.
Gauge do not indicate the actual value of the inspected part of the component.
They are used to determine whether the part is made within the specified limit.

## Slide 39: Plug gauges
Plug gauges are the limit gauges used for checking holes and consist of two cylindrical wear resistant plugs.
The plug made to the lower limit of the hole is known as ‘GO’ end and this will enter any hole which is not smaller than the lower limit allowed.
The plug made to the upper limit of the hole is known as ‘NO GO’ end and this will not enter any hole which is smaller than the upper limit allowed.

## Slide 40: Plug gauges

## Slide 41: Progressive plug gauges
For smaller through holes, both GO & NO GO gauges are on the same side separated by a small distance.
After the full length of GO portion enters the hole, further entry is obstructed by the NO GO portion if the hole is within the tolerance limits.

## Slide 42: Ring gauges
Ring gauges are used for gauging shafts. They are used in a similar manner to that of GO & NO GO plug gauges.
A ring gauge consists of a piece of metal in which a hole of required size is bored.

## Slide 43: SNAP (or) GAP GAUGES
A snap gauge usually consists of a plate or frame with a parallel faced gap of the required dimension.
Snap gauges can be used for both cylindrical as well as non-cylindrical work as compared to ring gauges which are conveniently used only for cylindrical work.
Double ended snap gauges can be used for sizes ranging from 3 to 100 mm. For sizes above 100 mm up to 250 mm a single ended progressive gauge may be used.

## Slide 44: SNAP (or) GAP GAUGES

## Slide 45: Limit Gauge

## Slide 46: Design of Limit Gauge

## Slide 47: Taylor’s Principle
Go Gauge should always be so designed that it will cover the maximum Metal Condition(MMC) of as many dimensions as possible in the same limit gauge, whereas Not Go gauge to cover the minimum metal condition of one dimension only.

## Slide 48: Taylor’s Principle

## Slide 49: GRADES OF TOLERANCE